## Slide 1
Version 1.0.3
2023.07
Glass Unpacking Loader
SECS/GEM Specification

## Slide 2
Revision History
Ver | Date | Chapter | Description
1.0.0 | 2023-04-15 |  | Draft
1.0.1 | 2023-04-23 |  | Data Item Modify
1.0.2 | 2023-07-03 |  | 시나리오 변경 및 Data 변경
1.0.3 | 2023-07-06 |  | 이벤트 추가 (CEID=1611 GlassStart, 1612 GlassEnd)

## Slide 3
CONTENTS
1. Unpacking Loader Equipment Specifications
2. CEID(Collected Event ID), SVID List
3. SECS-II Message Summary
4. SECS Message Stream & Functions
5. SCENARIO

## Slide 4
1. Unpacking Loader Equipment Specifications
1.1 Layout
Buffer
4단 Tray
Loading
간지 Tray
Unloading
Glass & Paper Transfer
EFEM Glass
Loading
USC

## Slide 5
EQPID | Module | Description | Location ID
AP-MR-01 | Tray Input CV | 4단 실트레이를 적재할 수 있는 투입 포트로 한 트레이에는 Glass 20장이 담겨 있음 | IP01
 | Tray Output CV | 간지, 폐글라스, 빈트레이를 적재하여 배출하는 포트 | OP01
 | Glass&Paper Transfer Unit | Glass, 간지 이재기 | TM01
 | BUFFER CV | Glass 이재기로부터 Glass 를 받아서 USC로 이동하는 CV | BF01
 | USC | Ultra Sonic Cleaner | USC01
1.2 Location ID LIST
Glass Unpacking
USC
IP01
OP01
TM01
BF01
USC01

## Slide 6
2.1 CEID(Collected Event ID)
CEID | Event | Description
1001 | ControlStateOffline | Equipment control state turn into OFFLINE
1002 | ControlStateLocal | Equipment control state turn into ONLINE LOCAL
1003 | ControlStateRemote | Equipment control state turn into ONLINE REMOTE
1015 | EquipmentConstantChanged | Equipment Constant is changed
1031 | AlarmDetected | alarm occurred
1032 | AlarmCleared | alarm cleared
1051 | EquipmentStateChanged | Equipment State is changed
1061 | OperationIDChanged | Events that occur when worker information registered in the HMI is changed
1101 | ModuleStart | Glass started operating on module
1102 | ModuleEnd | Glass completed operating on module
1201 | SubstrateLocationOccupied | Glass loaded into module
1202 | SubstrateLocationUnoccupied | Glass ejected into module
1301 | WorkStart | Tray의 첫 Glass를 TM01 Arm이 흡착
1311 | ProcessStart | Tray의 첫 Glass를 TM01 정위치 이동 완료
1312 | ProcessEnd | Tray의 마지막 Glass를 TM01 정위치 이동 완료
2.1.1 CEID LIST(1)

## Slide 7
2.1 CEID(Collected Event ID)
CEID | Event | Description
1401 | TrayLoadComplete | Tray loaded into input Port
1402 | TrayUnloadComplete | Tray loaded into output Port
1403 | TrayScrapComplete | Tray Scraped at input Port
1411 | TrayIDRead | Tray ID Read
1412 | TrayGlassOut | Glass move from Tray To Glass Transfer
1501 | PortOutOfService | Port Out Of Service
1502 | PortReadyToLoad | Port Ready To Load
1503 | PortTransferBolcked | Port Transfer Bolcked (Port loaded Tray)
1504 | PortReadyToUnload | Port Ready To Unload
1511 | PortStateChange | Port State Change
1601 | GlassIDRead | Glass ID Read
1602 | GlassScrapComplete | Glass Scrap Complete
1611 | GlassStart | Glass loaded into module at USC01
1612 | GlassEnd | Glass eject into module at USC01
2.1.1 CEID LIST(2)

## Slide 8
2.2 EC(Equipment Constant)
2.2.1 EC LIST(1)
ID | Name | Type | Unit | Min | Max | Def | Description
101 | EqpName | A |  | AP-MR-01 | AP-MR-01 | AP-MR-01 | Glass Unpacking Loader Equipment Name
102 | SessionID | U2 |  | 0 | 65535 | 0 | HSMS Session ID
103 | HsmsLinkTestInterval | U4 | sec | 10 | 86400 | 120 | HSMS Link Test Period
104 | EstablishCommnucationsTimeout | U4 | sec | 2 | 120 | 10 | Timeout for Establish Commnunication Message
105 | TimeFormat | U4 |  | 0 | 1 | 1 | 0 = 12 bytes format "YYMMDDhhmmss" 1 = 16 bytes format "YYYYMMDDhhmmsscc"
106 | T3TimeOut | U4 | sec | 1 | 120 | 45 | HSMS T3 Time
107 | T5TimeOut | U4 | sec | 1 | 240 | 10 | HSMS T5 Time
108 | T6TimeOut | U4 | sec | 1 | 240 | 5 | HSMS T6 Time
109 | T7TimeOut | U4 | sec | 1 | 240 | 10 | HSMS T7 Time
110 | T8TimeOut | U4 | sec | 1 | 240 | 5 | HSMS T8 Time
111 | UseS6F1Reply | Bo |  | false | true | false | true = need S6F1Reply (S6F2)

## Slide 9
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(1)
ID | Name | TYPE | Description
200 | CommState | U4 | 0 = Undefined 1 = Disabled 2 = Enabled / Not Communicating 3 = Equipment-Initiated Connect / Wait Delay 4 = Equipment-Initiated Connect / Wait CRA 5 = Host-Initiated Connect / Wait CR from Host 6 = Communicating
201 | ControlState | U4 | 1 = Equipment-Offline 2 = Attempt Online 3 = Host Offline 4 = Online-Local 5 = Online-Remote
202 | PreviousControlState | U4 | Previous Control state
203 | EqpState | U4 | 1 = Idle 2 = Run 3 = Maintenance 4 = Down
204 | PreviousEqpState | U4 | Previous Eqp State
205 | UserId | A | userId (current)
206 | PreviousUserId | A | last userid
210 | EventsEnabled | L | L,n n = # of events enabled 1.<CEID_1> … n.<CEID_n>
211 | AlarmsEnabled | L | L,n n = # of alarms enabled 1.<ALID_1> … n.<ALID_n>
212 | AlarmsSet | L | L,n n = # of alarms setted 1.<ALID_1> … n.<ALID_n>
220 | MDLN | A | “Unpacker” Equipment Model Type. Same data as returned by S1,F2
221 | SOFTREV | A | Software revision code.

## Slide 10
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(2)
ID | Name | TYPE | Description
11001 | Temp_Sensor_1 | F4 | Main Control Panel sensor temperature.
11002 | Main_power_voltage | F4 | Main power part valtage.
11003 | Travel_servo_torque | F4 | Travel servo motor torque
11004 | Travel_servo_speed | F4 | Travel servo motor speed
11005 | Hoist#1_servo_torque | F4 | Hoist#1 servo motor torque
11006 | Hoist#1_servo_speed | F4 | Hoist#1 servo motor speed
11007 | Hoist#2_servo_torque | F4 | Hoist#2 servo motor torque
11008 | Hoist#2_servo_speed | F4 | Hoist#2 servo motor speed

## Slide 11
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(3)
ID | Name | TYPE | Description
20001 | IP01_PortTransferState | U2 | 0 = None 1 = OutOfService 2 = TransferBlocked 3 = ReadyToLoad 4 = ReadyToUnload
20002 | IP01_PortState | U2 | Port의 사용 여부로 USC/ Arm/ BCR 등의 문제가 발생될 경우 투입을 제어하기 위해 Disable 상태가 될수 있음 0 = Disable / 1 = Enable
20003 | IP01_PortType | U2 | 1 = IN
20004 | IP01_TrayID | A | Tray ID for IP01
20011 | OP01_PortTransferState | U2 | 0 = None 1 = OutOfService 2 = TransferBlocked 3 = ReadyToLoad 4 = ReadyToUnload
20012 | OP01_PortState | U2 | Port의 사용 여부로 USC/ Arm/ BCR 등의 문제가 발생될 경우 투입을 제어하기 위해 Disable 상태가 될수 있음 0 = Disable / 1 = Enable
20013 | OP01_PortType | U2 | 2 = OUT
20014 | OP01_TrayID | A | Tray ID for OP01
20101 | TM01_GlassID | A | Glass ID for TM01
20102 | TM01_PortID | U2 | Tray PortID for TM01
20103 | TM01_TrayID | A | Tray ID for TM01
20104 | TM01_SlotNo | U2 | Tray SlotNo for TM01
20105 | TM01_LotID | A | LotID for TM01
20201 | BF01_GlassID | A | Glass ID for BF01
20202 | BF01_PortID | U2 | Tray PortID for BF01
20203 | BF01_TrayID | A | Tray ID for BF01
20204 | BF01_SlotNo | U2 | Tray SlotNo for BF01
20205 | BF01_LotID | A | LotID for BF01
20301 | USC01_GlassID | A | Glass ID for USC01
20302 | USC01_PortID | U2 | Tray PortID for USC01
20303 | USC01_TrayID | A | Tray ID for USC01
20304 | USC01_SlotNo | U2 | Tray SlotNo for USC01
20305 | USC01_LotID | A | LotID for USC01

## Slide 12
2.4 Report of Collection Events
2.4.1 DVID LIST(1)
ID | Name | TYPE | Description
301 | ALCD | Bi | Alarm code byte
302 | ALID | U4 | AlarmID of the most recent alarm to change state.
303 | ALTX | A | AlarmText of the most recent alarm to change state
304 | ECID | U4 | Equipment Constant ID
305 | ECNAME | A | Equipment Constant Name
306 | ECV | Any | Equipment Constant Value
310 | ModuleID | A | Substrate Location ID
311 | GlassID | A | Substrate ID
312 | PortID | U2 | Tray Port ID
313 | TrayID | A | Tray Carrier ID
314 | SlotNo | U2 | Tray Slot No
315 | IDReadStatus | U2 | 0 = Success 1 = Failure
316 | PortTransferState | U2 | 1 = OutOfService 2 = TransferBlocked 3 = ReadyToLoad 4 = ReadyToUnload
317 | PortState | U2 | 0 = Disable 1 = Enable
321 | WorkID | A | S3F41을 내린 후, S2F41로 WORK_START Command를 내릴 때,
322 | PreviousGlassID | A | S3F41로 전송된 Glass ID
323 | LotID | A | S3F41로 전송된 Lot ID

## Slide 13
2.5 Report of Collection Events
2.5.1 RPTID/CEID/VID List(1)
CEID | RPTID | VID | Contents
1001 1002 1003 |  |  | ControlStateOffline
 |  |  | ControlStateLocal
 |  |  | ControlStateRemote
 | 101 | 201 | ControlState
 |  | 202 | PreviousControlState
1015 |  |  | EquipmentConstantChanged
 | 102 | 304 | ECID
 |  | 305 | ECNAME
 |  | 306 | ECV
1031 1032 |  |  | AlarmDected
 |  |  | AlarmCleared
 | 103 | 310 | ModuleID
 |  | 301 | ALCD
 |  | 302 | ALID
 |  | 303 | ALTX
1051 |  |  | EquipmentStateChanged
 | 104 | 203 | EqpState
 |  | 204 | PreviousEqpState
1061 |  |  | OperationIDChanged
 | 105 | 205 | UserId
 |  | 206 | PreviousUserId
1101 1102 |  |  | ModuleStart
 |  |  | ModuleEnd
 | 106 | 310 | ModuleID
1201 1202 |  |  | SubstrateLocationOccupied
 |  |  | SubstrateLocationUnoccupied
 | 107 | 310 | ModuleID
 |  | 311 | GlassID

## Slide 14
2.5 Report of Collection Events
2.5.1 RPTID/CEID/VID List(2)
CEID | RPTID | VID | Contents
1301 1311 1312 |  |  | WorkStart
 |  |  | ProcessStart
 |  |  | ProcessEnd
 | 108 | 310 | ModuleID
 |  | 312 | PortID
 |  | 313 | TrayID
 |  | 321 | WorkID
1401 1402 1403 |  |  | TrayLoadComplete
 |  |  | TrayUnloadComplete
 |  |  | TrayScrapComplete
 | 109 | 312 | PortID
 |  | 313 | TrayID
1411 |  |  | TrayIDRead
 | 110 | 312 | PortID
 |  | 313 | TrayID
 |  | 315 | IDReadStatus
1412 |  |  | TrayGlassOut
 | 111 | 312 | PortID
 |  | 313 | TrayID
 |  | 314 | SlotNo
 |  | 322 | PreviousGlassID
 |  | 323 | LotID

## Slide 15
2.5 Report of Collection Events
2.5.1 RPTID/CEID/VID List(3)
CEID | RPTID | VID | Contents
1501 1502 1503 1504 |  |  | PortOutOfService
 |  |  | PortTransferBolcked
 |  |  | PortReadyToLoad
 |  |  | PortReadyToUnload
 | 112 | 312 | PortID
 |  | 316 | PortTransferState
1511 |  |  | PortStateChange
 | 113 | 312 | PortID
 |  | 317 | PortState
1601 |  |  | GlassIDRead
 | 114 | 310 | ModuleID
 |  | 311 | GlassID
 |  | 322 | PreviousGlassID
 |  | 315 | IDReadStatus
1602 |  |  | GlassScrapComplete
 | 115 | 310 | ModuleID
 |  | 311 | GlassID
1611 1612 |  |  | GlassStart
 |  |  | GlassEnd
 | 116 | 310 | ModuleID
 |  | 311 | GlassID
 |  | 312 | PortID
 |  | 313 | TrayID
 |  | 314 | SlotNo
 |  | 323 | LotID

## Slide 16
3. SECS-II Message Summary
Message | Direction | Description | Note
S*F0 | Host ↔ EQ | Abort Transaction | 
S1F1 | Host ↔ EQ | Are You There Request(R) | 
S1F2 | Host ↔ EQ | On-Line Data(D) | 
S1F3 | Host → EQ | Selected equipment status request | 
S1F4 | Host ← EQ | Selected Equipment status Data | 
S1F11 | Host → EQ | Status variable name-list request | 
S1F12 | Host ← EQ | Status Variable name-list reply | 
S1F13 | Host ↔ EQ | Establish communication request | 
S1F14 | Host ↔ EQ | Establish communication request Ack | 
S1F15 | Host → EQ | Request Off-line | 
S1F16 | Host ← EQ | Request Off-line Acknowledge | 
S1F17 | Host → EQ | Request On-line | 
S1F18 | Host ← EQ | Request On-line Acknowledge | 
S2F13 | Host → EQ | Equipment constant request | 
S2F14 | Host ← EQ | Equipment constant data | 
S2F15 | Host → EQ | New equipment constant send | 
S2F16 | Host ← EQ | New equipment constant Ack | 
S2F17 | Host ↔ EQ | Date and time request | 
S2F18 | Host ↔ EQ | Date and time data | 
S2F23 | Host → EQ | Trace Initialize Send | 
S2F24 | Host ← EQ | Trace Initialize Acknowledge | 
S2F25 | Host → EQ | Loop-back diagnostic request | 
S2F26 | Host ← EQ | Loopback Diagnostic Data | 
S2F29 | Host → EQ | Equipment constant name-list request | 
S2F30 | Host ← EQ | Equipment Constant Name-list | 
S2F31 | Host → EQ | Date and time send | 
S2F32 | Host ← EQ | Data and Time Set Acknowledge | 

## Slide 17
3. SECS-II Message Summary
Message | Direction | Description | Note
S2F33 | Host → EQ | Define Report | 
S2F34 | Host ← EQ | Define Report Acknowledge | 
S2F35 | Host → EQ | Link event report | 
S2F36 | Host ← EQ | Link event report acknowledge | 
S2F37 | Host → EQ | Enable/disable event report | 
S2F38 | Host ← EQ | Enable/disable event report acknowledge | 
S2F41 | Host → EQ | Host command send | 
S2F42 | Host ← EQ | Host command acknowledge | 
S2F49 | Host → EQ | Enhanced Remote Command Extension (ERC) | 
S2F50 | Host ← EQ | Enhanced Remote Command Ack. (ERCA) | 
S5F1 | Host ← EQ | Alarm report send | 
S5F2 | Host → EQ | Alarm report send acknowledge | 
S5F3 | Host → EQ | Enable/disable alarm send | 
S5F4 | Host ← EQ | Enable/disable alarm acknowledge | 
S5F5 | Host → EQ | List alarms request | 
S5F6 | Host ← EQ | List alarms data | 
S5F7 | Host → EQ | List enabled alarm request | 
S5F8 | Host ← EQ | List enabled alarm data | 
S6F1 | Host ← EQ | Trace Data Send | 
S6F2 | Host → EQ | Trace Data Acknowledge | 
S6F11 | Host ← EQ | Event report send | 
S6F12 | Host → EQ | Event report acknowledge | 
S9F1 | Host ← EQ | Unrecognized device ID | 
S9F3 | Host ← EQ | Unrecognized stream type | 
S9F5 | Host ← EQ | Unrecognized function type | 
S9F7 | Host ← EQ | Illegal data | 
S9F9 | Host ← EQ | Transaction timer timeout | 
S9F11 | Host ← EQ | Data too long | 

## Slide 18
3. SECS-II Message Summary
Message | Direction | Description | Note
S10F3 | H → E | Terminal displaysingle | 
S10F4 | H ← E | Terminal displaysingle acknowledge | 

## Slide 19
4. SECS Message Stream & Functions
4.1 Operational Concept
4.1.1 Data Format Length
I1 - Integer 1 Byte : From _128 to +127
I2 - Integer 2 Bytes : From _32,768 to +32,768
I4 - Integer 4 Bytes : From _2,157,483,648 to +2,157,483,648
I8 - Integer 8 Bytes : From _9,223,372,036,854,775,808 to +9,223,372,036,854,775,808
U1 - Unsigned 1 Bytes : From 0 to 255
U2 - Unsigned 2 Bytes : From 0 to 65,535
U4 - Unsigned 4 Bytes : From 0 to 4,294,967,295
U8 - Unsigned 8 Bytes : From 0 to 18,446,744,073,709,551,615
F4 - 4-byte floating point : From -3.40282347E+38F to 3.40282347E+38F
F8 - 8-byte floating point : From -1.7976931348623157E+308 to 1.7976931348623157E+308
Boolean : "False" or “True"
A[자릿수] - ASCII : Ex) a~z, A~Z, 0~9, _, space, (, ), etc

## Slide 20
4. SECS Message Stream & Functions
4.2 STREAM 1
■ S1, F2 On-line Data (H ← E) |  |  | 
 | Structure |  | 
 | L , 2 1. <A MDLN> 2. <A SOFTREV> |  | 
 | Dictionary |  | 
 | MDLN | Equipment ModelType, 6bytes max | Same data as returned by S1, F2
 | SOFTREV | Software revision code 6 bytes maximum | 
■ S1, F2 On-line Data (H → E) | 
 | Structure
 | L , 0
■ S1, F1 Are You There Request (H ↔ E) | 
 | Description
 | Establishes that the SECS-II link is operational and that the host and machine are online. The machine responds with its model number and software revision. The host responds with a null list. The equipment may use this message when using SECS-I as a "heartbeat" to detect communication failures. The equipment also uses this message in the Control State model when attempting to go online
 | Structure
 | Header only
■ S1, F3 Selected Equipment Status Request (H → E) |  |  | 
 | Structure |  | 
 | L , n 1. <U4 SVID> … n. <U4 SVID> |  | 
 | Dictionary |  | 
 | SVID | Status variable ID | Status variables may include any parameter that can be sampled in time such as temperature or quantity of a consumable.

## Slide 21
■ S1, F4 Selected Equipment Status Data(H ← E) |  |  | 
 | Structure |  | 
 | L , n 1. <* SV> n. <* SV> |  | 
 | Note |  | 
 | A zero-length U1 for SV means that the SVID does not exist. |  | 
 | Dictionary |  | 
 | SV | Status variable value | 
■ S1, F11 Status Variable Namelist Request ( (H → E) |  |  | 
 | Description |  | 
 | A request from the host to the machine to report the name and units of certain status variables, in the order requested. |  | 
 | Structure |  | 
 | L , n 1. <U4 SVID> … n. <U4 SVID> |  | 
 | Dictionary |  | 
 | SVID | Status variable ID | Status variables may include any parameter that can be sampled in time such as temperature or quantity of a consumable.
4. SECS Message Stream & Functions

## Slide 22
■ S1, F13 Establish Communications Request(H ↔ E) | 
 | Structure
 | L , 0
■ S1, F14 Establish Communications Request Acknowledge(H ↔ E) |  |  | 
 | Structure |  | 
 | L , 2 1. <Bi COMMACK> 2. L , 0 |  | 
 | Dictionary |  | 
 | COMMACK | Establish Communications Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied, Try Again 2-63 Reserved
■ S1, F12 Status Variable Namelist Reply(H ← E) |  |  | 
 | Structure |  | 
 | L , n 1. L , 3 1. <U4 SVID> 2. <A SVNAME> 3. <A UNITS> … n. L , 3 1. <U4 SVID> 2. <A SVNAME> 3. <A UNITS> |  | 
 | Dictionary |  | 
 | SVID | Status variable ID | Status variables may include any parameter that can be sampled in time such as temperature or quantity of a consumable.
 | SVNAME | Status Variable Name | 
 | UNITS | Units Identifier | As allowed by SEMI E5 Section 12.
4. SECS Message Stream & Functions

## Slide 23
■ S1, F14 Establish Communications Request Acknowledge(H ↔ E) |  |  | 
 | Structure |  | 
 | L , 2 1. <Bi COMMACK> 2. L , 2 1. <A MDLN> 2. <A SOFTREV> |  | 
 | Dictionary |  | 
 | COMMACK | Establish Communications Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied, Try Again 2-63 Reserved
 | MDLN | Equipment ModelType, 6bytes max | Same data as returned by S1, F2
 | SOFTREV | Software revision code 6 bytes maximum | 
■ S1, F13 Establish Communications Request(H ↔ E) |  |  | 
 | Description |  | 
 | Initiate an attempt to establish a SECS-II communications link at a logical level on power-up or after a break in the link. It is the first message sent after either of the above conditions. If no response is received from the host, the machine will periodically send a S1F13 message until a S1F14 with the correct COMMACK is received. |  | 
 | Structure |  | 
 | L , 2 1. <A MDLN> 2. <A SOFTREV> |  | 
 | Dictionary |  | 
 | MDLN | Equipment ModelType, 6bytes max | Same data as returned by S1, F2
 | SOFTREV | Software revision code 6 bytes maximum | 
4. SECS Message Stream & Functions

## Slide 24
■ S1, F18 On-line Control State Acknowledge(H ← E) |  |  | 
 | Structure |  | 
 | 1. <Bi OFLACK> |  | 
 | Dictionary |  | 
 | COMMACK | Establish Communications Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied, Try Again 2-63 Reserved
■ S1, F17 On-line Control State Request(H → E) | 
 | Description
 | The host requests that the equipment transition to the ON-LINE state.
 | Structure
 | Header only
■ S1, F16 Off-line Control State Acknowledge(H ← E) |  |  | 
 | Structure |  | 
 | 1. <Bi OFLACK> |  | 
 | Dictionary |  | 
 | COMMACK | Establish Communications Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied, Try Again 2-63 Reserved
■ S1, F15 Off-line Control State Request(H → E) | 
 | Description
 | The host requests that the equipment transition to the OFF-LINE state.
 | Structure
 | Header only
4. SECS Message Stream & Functions

## Slide 25
4.3 STREAM 2
■ S2, F13 Equipment Constant Request (H → E) |  |  | 
 | Description |  | 
 | A request from the host to report the value of certain equipment constants in a predefined order. |  | 
 | Structure |  | 
 | L , N 1. <U4 ECID> … n. <U4 ECID> |  | 
 | Dictionary |  | 
 | ECID | Equipment Constant ID | 
■ S2, F14 Equipment Constant Data(H ← E) |  |  | 
 | Structure |  | 
 | L , N 1. <* ECV> … n. <* ECV> |  | 
 | Dictionary |  | 
 | ECV | Equipment Constant Value | 
■ S2, F15 New Equipment Constant Send (H → E) |  |  | 
 | Description |  | 
 | Host updates the values of specified EC. If the host returns a non-zero EAC the equipment will not change the value of any ECID specified in the S2F15 body. |  | 
 | Structure |  | 
 | L , n 2. L , 2 <U4 ECID> <* ECV> … n. L , 2 <U4 ECID> <* ECV> |  | 
 | Dictionary |  | 
 | ECID | Equipment Constant ID | 
 | ECV | Equipment Constant Value | 
4. SECS Message Stream & Functions

## Slide 26
■ S2, F17 Date and Time Request (H ↔ E) | 
 | Description
 | The host requests that the equipment transition to the OFF-LINE state.
 | Structure
 | Header only
■ S2, F16 New Equipment Constant Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi EAC> |  | 
 | Dictionary |  | 
 | EAC | Equipment acknowledge code, 1 byte | 0 = Acknowledge 1 = Denied. At least one constant does not exist 2 = Denied. Busy 3 = Denied. At least one constant out of range >3 = Other equipment-specific error 4-63 Reserved
■ S2, F18 Date and Time Data (H ↔ E) |  |  | 
 | Structure |  | 
 | <A TIME> |  | 
 | Note |  | 
 | A zero-length item means no time exists. |  | 
 | Dictionary |  | 
 | TIME | Time of day, 12 or 16 bytes NOTE 4: The 16-byte format is currently optional. After January 1, 1998, the 16-byte format shall be required on new and updated implementations. Support for the 12-byte format shall be supported as a configurable option using the equipment constant TimeFormat. This is a format requirement only and does not imply either precision or accuracy. | If 12 bytes the format is YYMMDDhhmmss YY = Year 00 to 99 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 If 16 bytes the format is YYYYMMDDhhmmsscc YYYY = Year 0000 to 9999 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 cc = Centisecond 00 to 99
4. SECS Message Stream & Functions

## Slide 27
■ S2, F24 Trace Initialize Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi TIAACK> |  | 
 | Dictionary |  | 
 | TIAACK | Equipment acknowledgement code, 1 byte | 0 = Everything correct 1 = Too many SVIDs 2 = No more traces allowed 3 = Invalid period >3 = Equipment-specified error 4-63 Reserved
■ S2, F23 Trace Initialize Send (H → E) |  |  | 
 | Description |  | 
 | The host requests a time driven trace of specified status variables. If TOTSMP is zero, the machine will cancel an existing trace with the given TRID. |  | 
 | Structure |  | 
 | L , 5 1. <U4 TRID> 2. <A DSPER> 3. <U4 TOTSMP> 4. <U4 REPGSZ> 5. L , N 1. <U4 SVID> … 1. <U4 SVID> |  | 
 | Dictionary |  | 
 | TRID | Trace request ID | 
 | DSPER | Data sample period. DSPER has two allowable formats: | Format 1: hhmmss, 6 bytes Format 2: hhmmsscc, 8 bytes Where “hh” is hours, “mm” is minutes, “ss” is seconds’ and “cc” is centiseconds. Equipment shall either (1) support only Format 1, or (2) support both Format 1 and Format 2. Equipment shall document which formats it accepts. Equipment which supports Format 2 need not necessarily support a minimum DSPER of 1 centisecond, nor a trace resolution of 1 centisecond, but equipment suppliers shall document its trace performance limits.
 | TOTSMP | Total samples to be made | 
 | REPGSZ | Reporting group size | 
 | SVID | Status variable ID | Status variables may include any parameter that can be sampled in time such as temperature or quantity of a consumable.
4. SECS Message Stream & Functions

## Slide 28
■ S2, F26 Loop-back Diagnostic Data (H ↔ E) |  |  | 
 | Structure |  | 
 | <** ABS> |  | 
 | Dictionary |  | 
 | ABS | Any binary string | 
■ S2, F29 Equipment Constant Name list Request (H → E) |  |  | 
 | Description |  | 
 | A request from the host to the equipment to retrieve information regarding the specified equipment constants. A zero length list (n = 0) means to send information for all ECID. |  | 
 | Structure |  | 
 | L , n 1. <U4 ECID> … n. <U4 ECID> |  | 
 | Dictionary |  | 
 | ECID | Equipment Constant ID | 
■ S2, F25 Loop-back Diagnostic Request (H ↔ E) |  |  | 
 | Description |  | 
 | A diagnostic message for checkout of protocol and communication circuits. The message sent is echoed back. |  | 
 | Structure |  | 
 | <* ABS> |  | 
 | Dictionary |  | 
 | ABS | Any binary string | 
4. SECS Message Stream & Functions

## Slide 29
■ S2, F30 Equipment Constant Name list (H ← E) |  |  | 
 | Structure |  | 
 | L , n 1. L , 6 1. <U4 ECID> 2. <A ECNAME> 3. <* ECMIN> 4. <* ECMAX> 5. <* ECDEF> 6. <A UNITS> … n. L , 6 1. <U4 ECID> 2. <A ECNAME> 3. <* ECMIN> 4. <* ECMAX> 5. <* ECDEF> 6. <A UNITS> |  | 
 | Note |  | 
 | Zero length ASCII items for ECNAME, ECMIN, ECMAX, ECDEF and UNITS indicates that the ECID does not exist. |  | 
 | Dictionary |  | 
 | ECID | Equipment Constant ID | 
 | ECNAME | Equipment constant name | 
 | ECMIN | Equipment constant minimum value | 
 | ECMAX | Equipment constant maximum value | 
 | ECDEF | Equipment constant default value | 
 | UNITS | Units Identifier | As allowed by SEMI E5 Section 12.
4. SECS Message Stream & Functions

## Slide 30
■ S2, F31 Date and Time Set Request (H → E) |  |  | 
 | Description |  | 
 | The host instructs the equipment to set its time base to the specified value. |  | 
 | Structure |  | 
 | <A TIME> |  | 
 | Dictionary |  | 
 | TIME | Time of day, 12 or 16 bytes NOTE 4: The 16-byte format is currently optional. After January 1, 1998, the 16-byte format shall be required on new and updated implementations. Support for the 12-byte format shall be supported as a configurable option using the equipment constant TimeFormat. This is a format requirement only and does not imply either precision or accuracy. | If 12 bytes the format is YYMMDDhhmmss YY = Year 00 to 99 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 If 16 bytes the format is YYYYMMDDhhmmsscc YYYY = Year 0000 to 9999 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 cc = Centisecond 00 to 99
■ S2,F32 Date and Time Set Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi TIACK> |  | 
 | Dictionary |  | 
 | TIAACK | Equipment acknowledgement code, 1 byte | 0 = Everything correct 1 = Too many SVIDs 2 = No more traces allowed 3 = Invalid period >3 = Equipment-specified error 4-63 Reserved
4. SECS Message Stream & Functions

## Slide 31
■ S2, F33 Define Report (H → E) |  |  | 
 | Structure |  | 
 | L , 2 1. <U4 DATAID> 2. L , a 1. L , 2 1. <U4 RPTID> 2. L , b 1. <U4 VID> … b. <U4 VID> … a. L , 2 1. <U4 RPTID> 2. L , c 1. <U4 VID> … c. <U4 VID> |  | 
 | Note |  | 
 | A zero-length list following DATAID deletes all report definitions and associated links. See S2, F35. A zero-length list following RPTID deletes report type RPTID. All CEID links to this RPTID are also deleted. |  | 
 | Dictionary |  | 
 | DATAID | Data ID | 
 | RPTID | Report ID | 
 | VID | Variable ID | 
■ S2, F34 Define Report Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi DRACK> |  | 
 | Dictionary |  | 
 | DRACK | Define Report Acknowledge Code, 1 byte | 0 = Accept 1 = Denied. Insufficient space 2 = Denied. Invalid format 3 = Denied. At least one RPTID already defined 4 = Denied. At least VID does not exist >4 = Other errors 5-63 Reserved
4. SECS Message Stream & Functions

## Slide 32
■ S2, F35 Link Event Report (H → E) |  |  | 
 | Description |  | 
 | The host links Report IDs (RPTID) to Collection event IDs (CEID). These linked event reports default to "disabled" upon linking. That is, the occurrence of an event would not cause the report to be sent until enabled. See S2, F37 for enabling events. |  | 
 | Structure |  | 
 | L , 2 1. <U4 DATAID> 2. L , a 1. L , 2 1. <U4 CEID> 2. L , b 1. <U4 RPTID> … b. <U4 RPTID> … a. L , 2 1. <U4 CEID> 2. L , c 1. <U4 RPTID> … c. <U4 RPTID> |  | 
 | Note |  | 
 | A zero-length list following CEID deletes all report links to that event. |  | 
 | Dictionary |  | 
 | DATAID | Data ID | 
 | CEID | Collected event ID | 
 | RPTID | Report ID | 
■ S2, F36 Link Event Report Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi DRACK> |  | 
 | Dictionary |  | 
 | DRACK | Define Report Acknowledge Code, 1 byte | 0 = Accept 1 = Denied. Insufficient space 2 = Denied. Invalid format 3 = Denied. At least one RPTID already defined 4 = Denied. At least VID does not exist >4 = Other errors 5-63 Reserved
4. SECS Message Stream & Functions

## Slide 33
■ S2, F37 Enable/Disable Event Report (H → E) |  |  | 
 | Description |  | 
 | Host requests to enable or disable reporting for a list of Collection events (CEID). |  | 
 | Structure |  | 
 | L , 2 1. <Bo CEED> 2. L , n 1. <U4 CEID> … n. <U4 CEID> |  | 
 | Note |  | 
 | A zero-length list (n = 0) means all CEID. |  | 
 | Dictionary |  | 
 | CEED | Collection event or trace enable/disable code, 1 byte | FALSE = Disable TRUE = Enable
 | CEID | Collected event ID | 
■ S2, F38 Enable/Disable Event Report Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi ERACK> |  | 
 | Dictionary |  | 
 | ERACK | Enable/Disable Event Report Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied. At least one CEID does not exist >1 = Other Errors 2-63 Reserved
4. SECS Message Stream & Functions

## Slide 34
■ S2, F41 Host Command Send(H → E) |  |  | 
 | Description |  | 
 | The host sends a request to the equipment to perform the specified command with the relevant parameters. |  | 
 | Structure |  | 
 | L 2 1. <A RCMD> 2. L , 1 1. L , 2 1. <A CPNAME> 2. <A CPVAL> |  | 
 | Dictionary |  | 
 | RCMD | Remote command code or string | 
 | CPNAME | Parameter name | 
 | CPVAL | Command Parameter Value. | 
4. SECS Message Stream & Functions

## Slide 35
■ S2, F42 Host Command Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | L , 2 1. <Bi HCACK> 2. L , n 1. L , 2 1. <A CPNAME> 2. <* CEPACK> … n. L , 2 1. <A CPNAME> 2. <* CEPACK> |  | 
 | Dictionary |  | 
 | HCACK | Host Command Parameter Acknowledge Code, 1 byte | 0 = Acknowledge, command has been performed 1 = Command does not exist 2 = Cannot perform now 3 = At least one parameter is invalid 4 = Acknowledge, command will be performed with completion signaled later by an event 5 = Rejected, Already in Desired Condition 6 = No such object exists 7-63 Reserved
 | CPNAME | Recipe name | 
 | CEPACK | Command Enhanced Parameter cknowledge. If a specific value of CPNAME is defined to have a CEPVAL that is a LIST, then CEPACK shall have the same structure as the corresponding list format of CEPVAL as used in S2,F49. Otherwise CEPACK will be a 1 byte integer. Enumerated: | 0 = No error 1 = Parameter name (CPNAME) does not exist 2 = Illegal value specified for CEPVAL 3 = Illegal format specified for CEPVAL 4 = Parameter name (CPNAME) not valid as used 5-63 Reserved
4. SECS Message Stream & Functions

## Slide 36
■ S2, F49 Enhanced Remote Command Extension (ERC) (H → E) |  |  | 
 | Description |  | 
 | The host requests an object to perform the specified remote command with its parameters |  | 
 | Structure |  | 
 | L 4 1. <A DATAID> 2. <A OBJSPEC> 3. <A RCMD> 4. L , n # of Parameter Groups 1. L , 2 1. <A CPNAME> 2. <CEPVAL> 2. L , 2 1. <A CPNAME> 2. <CEPVAL> : : n. L , 2 1. <A CPNAME> 2. <CEPVAL> |  | 
 | Dictionary |  | 
 | DATAID | Data ID | 
 | OBJSPEC | A text string that has an internal format and that is used to point to a specific object instance. The string is formed out of a sequence of formatted substrings, each specifying an object’s type and identifier. The substring format has the following four fields: object type, colon character ‘:’, object identifier, greater-than symbol ‘>’ where the colon character ‘:’ is used to terminate an object type and the greater than symbol ‘>’ is used to terminate an identifier field. The object type field may be omitted where it may be otherwise determined. The final ‘>’ is optional. | 
 | RCMD | Remote command code or string | 
 | CPNAME | Parameter name | 
 | CEPVAL | Command Parameter Value. | 
4. SECS Message Stream & Functions

## Slide 37
■ S2, F50 Enhanced Remote Command Ack. (ERCA) (H ← E) |  |  | 
 | Structure |  | 
 | L , 2 1. <Bi HCACK> 2. L , n # of Parameter Groups 1. L , 2 1. <A CPNAME> 2. <* CEPACK> : : n. L , 2 1. <A CPNAME> 2. <* CEPACK> |  | 
 | Dictionary |  | 
 | HCACK | Host Command Parameter Acknowledge Code, 1 byte | 0 = Acknowledge, command has been performed 1 = Command does not exist 2 = Cannot perform now 3 = At least one parameter is invalid 4 = Acknowledge, command will be performed with completion signaled later by an event 5 = Rejected, Already in Desired Condition 6 = No such object exists 7-63 Reserved
 | CPNAME | Recipe name | 
 | CEPACK | Command Enhanced Parameter cknowledge. If a specific value of CPNAME is defined to have a CEPVAL that is a LIST, then CEPACK shall have the same structure as the corresponding list format of CEPVAL as used in S2,F49. Otherwise CEPACK will be a 1 byte integer. Enumerated: | 0 = No error 1 = Parameter name (CPNAME) does not exist 2 = Illegal value specified for CEPVAL 3 = Illegal format specified for CEPVAL 4 = Parameter name (CPNAME) not valid as used 5-63 Reserved
4. SECS Message Stream & Functions

## Slide 38
4.4 STREAM 3
■ S3, F41 Work Order Request (H → E) | 
 | Description
 | host에서 work관련 모든 정보 message
 | Structure
 | L , 3 1. <A 'WorkOrder'> 2. <A EQPID> 3. <L [1] 1. <L [2] 1. <A [1] '0'> --------------- job 순서 2. <L [1] 1. <L [6] 1. <L [2] 1. <A [10] 'sorterType'> --------------- sorter 종류 2. <A> > 2. <L [2] 1. <A [8] 'inPortId’> 2. <A [1] '1'> --------------- in port id > 3. <L [2] 1. <A [8] 'inCarrId’> 2. <A [6] 'CST022'> --------------- in carrier id > 4. <L [2] 1. <A [9] outPortId’> 2. <A [1] ‘2'> --------------- out port id > 5. <L [2] 1. <A [9] outCarrId’> 2. <A [6] 'CST011'> --------------- out carrier id > 6. <L [1] 1. <L [2] 1. <L [2] 1. <A [4] 'PPID'> 2. <A [6] 'RCP001'> --------------- ppid > 2. <L [2] 1. <A 'SLOT_DATA'> --------------- slot정보(slot count로 list구성) 2. <L [n] slot count 1. <L [7] 1. <L [2] 1. <A [12] 'inCarrSlotNo'> 2. <A [1] '6'> --------------- in carrier slotno >
4. SECS Message Stream & Functions

## Slide 39
 | 2. <L [2] 1. <A [10] 'manualInsp'> 2. <A [1] 'N'> --------------- 자주검사여부 > 3. <L [2] 1. <A [10] 'prodMtrlId'> 2. <A [9] 'GLASS_006'> --------------- glass id > 4. <L [2] 1. <A [9] 'slotState'> 2. <A [1] '1'> --------------- slot state > 5. <L [2] 1. <A [13] 'outCarrSlotNo’> 2. <A [1] '6'> --------------- out carrier slotno > 6. <L [2] 1. <A [5] 'lotId'> 2. <A [13] 'LOT_230217005'> --------------- lot id > 7. <L [2] 1. <A [8] 'mtrlFace'> 2. <A [3] 'TBT'> --------------- top/bottom여부(TTT:top, TBT:bottom) > > > > > > > > > > |  | 
 | Dictionary |  | 
 | EQPID | 장비아이디 | ‘AP-MR-01’
 | slot count | Tray 1개 당 Glass 20개 | 
■ S3, F42 Work Order Request Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi ACKC5> |  | 
 | Dictionary |  | 
 | ACKC5 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved
4. SECS Message Stream & Functions

## Slide 40
4.5 STREAM 5
■ S5, F1 Alarm Report Send (H ← E) |  |  | 
 | Description |  | 
 | This message is sent whenever an alarm changes states to "Set" or "Clear" |  | 
 | Structure |  | 
 | L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> |  | 
 | Dictionary |  | 
 | ALCD | Alarm code byte | bit 8 = 1 means alarm set bit 8 = 0 means alarm cleared bit 7-1 is alarm category 0 = Not used 1 = Personal safety 2 = Equipment safety 3 = Parameter control warning 4 = Parameter control error 5 = Irrecoverable error 6 = Equipment status warning 7 = Attention flags 8 = Data integrity >8 = Other categories
 | ALID | Alarm identification | 
 | ALTX | Alarm text limited to 40 characters | 
■ S5, F2 Alarm Report Acknowledge (H → E) |  |  | 
 | Structure |  | 
 | <Bi ACKC5> |  | 
 | Dictionary |  | 
 | ACKC5 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved
4. SECS Message Stream & Functions

## Slide 41
■ S5, F3 Enable/Disable Alarm Send (H → E) |  |  | 
 | Description |  | 
 | This message enables or disables an alarm from being reported to the host. Some alarms (safety related) are not controllable in this way. |  | 
 | Structure |  | 
 | L , 2 1. <Bi ALED> 2. <U4 ALID> |  | 
 | Dictionary |  | 
 | ALED | Alarm enable/disable code, 1 byte | bit 8 = 1 means enable alarm bit 8 = 0 means disable alarm
 | ALID | Alarm identification | 
■ S5, F4 Enable/Disable Alarm Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi ACKC5> |  | 
 | Dictionary |  | 
 | ACKC5 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved
4. SECS Message Stream & Functions

## Slide 42
■ S5, F5 List Alarms Request (H → E) |  |  | 
 | Description |  | 
 | The host requests the equipment to send information on currently defined alarms. |  | 
 | Structure |  | 
 | <U4 ALID1, . . ., ALIDn> |  | 
 | Note |  | 
 | A zero-length item (n = 0) means send all possible alarms regardless of the state of ALED. |  | 
 | Dictionary |  | 
 | ALID | Alarm identification | 
■ S5, F6 List Alarms Data (H ← E) |  |  | 
 | Structure |  | 
 | L , m 1. L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> … m. L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> |  | 
 | Note |  | 
 | If m = 0, no response can be made. A zero-length item returned for ALCD or ALTX means that value does not exist. |  | 
 | Dictionary |  | 
 | ALCD | Alarm code byte | bit 8 = 1 means alarm set bit 8 = 0 means alarm cleared bit 7-1 is alarm category 0 = Not used 1 = Personal safety 2 = Equipment safety 3 = Parameter control warning 4 = Parameter control error 5 = Irrecoverable error 6 = Equipment status warning 7 = Attention flags 8 = Data integrity >8 = Other categories
 | ALID | Alarm identification | 
 | ALTX | Alarm text limited to 40 characters | 
4. SECS Message Stream & Functions

## Slide 43
■ S5, F7 List Alarms Request (H → E) | 
 | Description
 | List alarms which are enabled.
 | Structure
 | Header only
■ S5, F8 List Alarms Data (H ← E) |  |  | 
 | Structure |  | 
 | L , m 1. L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> … m. L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> |  | 
 | Note |  | 
 | If m = 0, no response can be made. A zero-length item returned for ALCD or ALTX means that value does not exist. |  | 
 | Dictionary |  | 
 | ALCD | Alarm code byte | bit 8 = 1 means alarm set bit 8 = 0 means alarm cleared bit 7-1 is alarm category 0 = Not used 1 = Personal safety 2 = Equipment safety 3 = Parameter control warning 4 = Parameter control error 5 = Irrecoverable error 6 = Equipment status warning 7 = Attention flags 8 = Data integrity >8 = Other categories
 | ALID | Alarm identification | 
 | ALTX | Alarm text limited to 40 characters | 
4. SECS Message Stream & Functions

## Slide 44
4.6 STREAM 6
4. SECS Message Stream & Functions
■ S6, F1 Trace Data Send (H ← E) |  |  | 
 | Description |  | 
 | Trace Samples configured with S2, F23 messages are sent to the host in these messages. |  | 
 | Structure |  | 
 | L , 4 1. <U4 TRID> 2. <U4 SMPLN> 3. <A STIME> L, n 1. <* SV> … n. <* SV> |  | 
 | Dictionary |  | 
 | TRID | Trace request ID | 
 | SMPLN | Sample number | 
 | STIME | Sample time, 12 or 16 bytes. NOTE 3: The 16-byte format is currently optional. After January 1, 1998, the 16-byte format shall be required on new and updated implementations. Support for the 12-byte format shall be supported as a onfigurable option using the equipment constant TimeFormat. This is a format requirement only and does not imply either precision or accuracy. | If 12 bytes the format is YYMMDDhhmmss YY = Year 00 to 99 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 If 16 bytes the format is YYYYMMDDhhmmsscc YYYY = Year 0000 to 9999 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 cc = Centisecond 00 to 99
 | SV | Status variable value | 
■ S6, F2 Trace Data Acknowledge (H → E) |  |  | 
 | Structure |  | 
 | <Bi ACKC6> |  | 
 | Dictionary |  | 
 | ACKC6 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved

## Slide 45
■ S6, F11 Event Report Send (H ← E) |  |  | 
 | Description |  | 
 | The machine sends a defined, event linked and enabled group of reports to the host on a linked event. This is a message that possibly requires a preceding S6, F5/F6 multiblock enquire/grant transaction. |  | 
 | Structure |  | 
 | L , 3 1. <U4 DATAID> 2. <U4 CEID> 3. L , a 1. L , 2 1. <U4 RPTID> 2. L , b 1. <*V> … b. <*V> … a. L , 2 1. <U4 RPTID> 2. L , c 1. <*V> … c. <*V> |  | 
 | Note |  | 
 | If there are no reports linked to the event a "null" report is assumed. A zero-length list for # of reports (a = 0) means there are no reports linked to the given CEID. |  | 
 | Dictionary |  | 
 | DATAID | Data ID | 
 | CEID | Collected event ID | 
 | RPTID | Report ID | 
 | V | Variable data | 
■ S6, F12 Event Report Acknowledge (H → E) |  |  | 
 | Structure |  | 
 | <Bi ACKC6> |  | 
 | Dictionary |  | 
 | ACKC6 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved
4. SECS Message Stream & Functions

## Slide 46
4.7 STREAM 9
■ S9, F1 Unrecognized Device ID (H ← E) |  |  | 
 | Description |  | 
 | Device ID specified in block header is not defined in the machine. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
■ S9, F3 Unrecognized Stream Type (H ← E) |  |  | 
 | Description |  | 
 | Machine does not recognize the stream type in the message block header. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
■ S9, F5 Unrecognized Function Type (H ← E) |  |  | 
 | Description |  | 
 | Machine does not recognize the stream type in the message block header. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
4. SECS Message Stream & Functions

## Slide 47
■ S9, F9 Transaction Timer Timeout (H ← E) |  |  | 
 | Description |  | 
 | This error specifies that a transaction / receive timer has timed out and the transaction aborted. The host system should respond to this message in a suitable manner to keep the system operational |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
■ S9, F11 Data Too Long (H ← E) |  |  | 
 | Description |  | 
 | The machine has been sent more data than it can handle. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
■ S9, F7 Illegal Data (H ← E) |  |  | 
 | Description |  | 
 | This error signifies that the stream and function were correctly interpreted but the associated data was not. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
4. SECS Message Stream & Functions

## Slide 48
4.8 STREAM 10
■ S10, F3 Terminal Display (Single) (H → E) |  |  | 
 | Description |  | 
 | The host requests a text message be displayed on the machine. |  | 
 | Structure |  | 
 | L , 2 1. <Bi TID> 2. <A TEXT> |  | 
 | Dictionary |  | 
 | TID | Terminal number, 1 byte | 0 = Single or main terminal >0 = Additional terminals at the same equipment
 | TEXT | A single line of characters | 
4. SECS Message Stream & Functions
■ S10, F4 Terminal Display (Single) Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi ACKC10> |  | 
 | Dictionary |  | 
 | ACKC10 | Acknowledge Code, 1 byte | 0 = Accepted for display 1 = Message will not be displayed 2 = Terminal not available 3-63 Reserved

## Slide 49
5. SCENARIO
5.1 Message Scenario
■ Host Attempts to Establish Communications
Comment | Host | Equipment | Comment
Establish Communications | S1, F13 |  | 
 |  |  | Communications state is enabled (any substate)
 |  | S1, F14 | Reply COMMACK = Accept and Communications state = COMMUNICATING
Comment | Host | Equipment | Comment
 |  |  | Communications State = NOT COMMUNICATING
 |  | S1, F13 | [LOOP] [LOOP] -- SEND Establish Communications Request
Establish Communications Acknowledge | S1, F14 |  | [IF] S1, F14 received without timeouts [THEN] exit loop -- SEND [ELSE] Delay for interval in EstablishCommunications Timeout [ENDIF] [END_LOOP]--SEND [IF] COMMACK = Accept [THEN] Communications state = Communicating exit loop -- [ELSE] Reset timer for delay, and delay for interval specified in EstablishCommunications Timeout [ENDIF] [END_LOOP]
■ Equipment Attempts To Establish Communications and Host Acknowledges

## Slide 50
Comment | Host | Equipment | Comment
 |  |  | Communications State = NOT COMMUNICATING
 |  | S1, F13 | Establish Communications Request
Establish Communications Request | S1, F13 |  | 
Reply COMMACK = Accept | S1, F14 |  | S1, F14 received from Host and Communications established* and Communications state = COMMUNICATING
 |  | S1, F14 | Reply COMMACK = Accept*
■ Equipment Receives S1, F14 From Host Before Sending S1, F14
Comment | Host | Equipment | Comment
 |  |  | Communications State = NOT COMMUNICATING
 |  | S1, F13 | Establish Communications Request
Establish Communications Request | S1, F13 |  | 
Reply COMMACK = Accept |  | S1, F14 | Reply COMMACK = Accept* Communications established** and Communications state = COMMUNICATING
 | S1, F14 |  | S1, F14 received from Host
■ Equipment Sends S1, F14 To Host Before Receiving S1, F14
5. SCENARIO

## Slide 51
Comment | Host | Equipment | Comment
Send report definitions | S2, F33 |  | DATAIDs, RPTIDs and VIDs received
 |  | S2, F34 | DRACK* = 0 the reports are OK
[ENDIF] |  |  | 
Link reports to events | S2, F35 |  | CEIDs and the corresponding RPTIDs are received
 |  | S2, F36 | LRACK = 0 the event linkages are acceptable.
Enable specific collection events | S2, F37 |  | Enable/disable codes (CEEDs) and the respective event reporting CEIDs received.
 |  | S2, F38 | ERACK = 0 OK, will generate the specified reports when the appropriate collection events happen.
■ Collection Event Reporting Set-up
5. SCENARIO

## Slide 52
Comment | Host | Equipment | Comment
Host requests report of selected status variable values. | S1, F3 |  | 
 |  | S1, F4 | Equipment responds with the requested status variable data.
■ Request Equipment Status Variable Namelist
Comment | Host | Equipment | Comment
Host requests equipment to identify selected status variables. | S1, F11 |  | 
 |  | S1, F12 | Equipment responds with the requested status variable descriptions.
■ Request Equipment Status Report
5. SCENARIO

## Slide 53
Comment | Host | Equipment | Comment
Enable/Disable Alarm | S5, F3 |  | 
 |  | S5, F4 | Acknowledge
■ Enable/Disable Alarms
Comment | Host | Equipment | Comment
Request alarm data/text | S5, F5 |  | 
 |  | S5, F6 | Send alarm data/text
■ Enable/Disable Alarms
Comment | Host | Equipment | Comment
Request enabled alarms | S5, F7 |  | 
 |  | S5, F8 | Send alarm data/text
■ Enable/Disable Alarms
Comment | Host | Equipment | Comment
 |  | S5, F1 | Send alarm report (if enabled)
Acknowledge | S5, F2 |  | 
 |  | S6, F11 | Send event report (if enabled)
Acknowledge | S6, F12 |  | 
■ Send Alarm Report
5. SCENARIO

## Slide 54
Comment | Host | Equipment | Comment
Host Command Send | S2, F41 |  | Remote Command Message
 |  | S2, F42 | Host Command Acknowledge
 |  | S6, F11 | [IF] Command Accepted (HCACK = 0 or 4) [THEN] State change or other collection event Occurrence
Event Report Acknowledge | S6, F12 |  | 
■ Host sends a remote command message
Comment | Host | Equipment | Comment
Host sends equip-ment constants. | S2, F15 |  | 
 |  | S2, F16 | EAC = 0 equipment sets constants
■ Host Equipment Constants Request
Comment | Host | Equipment | Comment
Host constant request | S2, F13 |  | 
 |  | S2, F14 | Equipment constant data, see note below
■ Host sends a remote command message
5. SCENARIO

## Slide 55
Comment | Host | Equipment | Comment
Host constant namelist request | S2, F29 |  | 
 |  | S2, F30 | Equipment
■ Operator Changes Equipment Constant
Comment | Host | Equipment | Comment
 |  |  | Operator changes equipment constant at equipment operator console.
 |  | S6, F11 | Equipment reports equipment constant change.
Host acknowledges event | S6, F12 |  | 
■ Host Equipment Constant Namelist Request
Comment | Host | Equipment | Comment
 |  |  | Material is sent or received at an equipment port.
 |  | S6, F11 | Send Collection event to host
Host acknowledges | S6, F12 |  | 
■ Material Movement
5. SCENARIO

## Slide 56
■ Terminal Services
Comment | Host | Equipment | Comment
Host sends textual information to equipment for display to the operator on terminal x. | S10, F3 |  | 
 |  | S10, F4 | Equipment acknowledges request to display text (equipment sets unrecognized message indicator).
 |  |  | Operator indicates message recognition (equipment clears unrecognized message indicator).
 |  | S6, F11 | Message recognition event. (see Event Data Collection for details).
Host acknowledges Optional: | S6, F12 |  | 
5. SCENARIO

## Slide 57
Comment | Host | Equipment | Comment
Host sends textual information to equipment for display to the operator on terminal x. | S10, F3 |  | 
 |  | S10, F4 | Equipment acknowledges request to display text (equipment sets unrecognized message indicator).
Host sends textual information to equipment for display to the operator on ter-minal x. This message overwrites the first one sent by the host since it is still unrecognized. | S10, F3 |  | 
 |  | S10, F4 | Equipment acknowledges request to display text (equipment sets unrecognized message indicator).
 |  |  | Operator indicates message recognition. (Equipment clears unrecognized message indicator).
 |  | S6, F11 | Message recognition event
Host acknowledges | S6, F12 |  | 
5. SCENARIO

## Slide 58
Comment | Host | Equipment | Comment
 |  | S2, F17 | Equipment requests a time value from the host.
Host responds with a TIME value | S2, F18 |  | Equipment sets its internal time reference to the value of TIME received from the host.
■ Host Instructs Equipment to Set Time
Comment | Host | Equipment | Comment
Host instructs equip-ment to set its time. | S2, F31 |  | 
 |  | S2, F32 | The equipment sets its internal time reference to the value of TIME received from the host and acknowledges completion.
■ Host Requests Equipment’s Current Time Value
Comment | Host | Equipment | Comment
Host requests equipment time.. | S2, F17 |  | 
 |  | S2, F18 | Equipment returns its internal time reference value to the host.
■ Equipment Requests TIME (Optional Scenario)
5. SCENARIO

## Slide 59
Comment | Host | Equipment | Comment
 |  |  | Operator actuates ON-LINE switch when equipment OFF_LINE state is active.
 |  | S1, F1 | Equipment request ON-LINE.
Host grants ON-LINE | S1, F2 |  | 
 |  | S6, F11 | "Control State LOCAL (or REMOTE)" collection event.
Acknowledge | S6, F12 |  | 
Comment | Host | Equipment | Comment
 |  |  | Operator actuates OFFLINE switch when equipment ON_LINE state is active.
 |  | S6, F11 | "Equipment request OFF-LINE" event.
Acknowledge | S6, F12 |  | 
■ Host Denies ON-LINE
Comment | Host | Equipment | Comment
 |  |  | Operator actuates ONLINE switch when equipment OFF_LINE state is active.
 |  | S1, F1 | Equipment requests ON-LINE.
Host denies ON-LINE | S1, F0 |  | 
■ Operator Sets OFF-LINE
■ Host Accepts ON-LINE
5. SCENARIO

## Slide 60
Comment | Host | Equipment | Comment
Host request OFF-LINE. | S1, F15 |  | 
 |  |  | [IF] Equipment is OFF-LINE
 |  | S1, F0 | [THEN] Equipment does not process requests.
 |  |  | [ELSE] Equipment ON-LINE
 |  | S1, F16 | Equipment acknowledges request and transitions to OFF-LINE.
 |  | S6, F11 | "Equipment OFF-LINE" event.
Acknowledge | S6, F12 |  | 
 |  |  | [END_IF]
Comment | Host | Equipment | Comment
 |  |  | Operator sets switch from LOCAL to REMOTE.
 |  | S6, F11 | "Control State REMOTE" event..
Acknowledge | S6, F12 |  | 
■ Operator Sets REMOTE
■ Operator Sets LOCCAL
Comment | Host | Equipment | Comment
` |  |  | Operator sets switch from REMOTE to LOCAL.
 |  | S6, F11 | "Control State LOCAL" event..
Acknowledge | S6, F12 |  | 
■ Host Sets OFF-LINE
5. SCENARIO

## Slide 61
Comment | Host | Equipment | Comment
Host requests ON-LINE. | S1, F17 |  | 
 |  |  | [IF] Equipment is HOST OFF-LINE state not active.
 |  | S1, F18 | [THEN] Equipment denies request (ONLACK = 0).
 |  |  | [ELSE] Equipment HOST OFF-LINE state is active.
 |  | S1, F18 | Equipment acknowledges request (ONLACK = 0).
 |  | S6, F11 | "Control state LOCAL (or REMOTE)" event.
Acknowledge | S6, F12 |  | 
 |  |  | [END_IF]
■ Host Sets OFF-LINE
5. SCENARIO

## Slide 62
5.2 Connection Establishment Scenario
HOST
TOOL
Establish Communication Request
Establish Communication
Request Acknowledge
<COMMACK=0,1>
S1F13
S1F14
Request Online
S1F17
S1F18
Online Acknowledge
<ONLACK=0,1,2>
COMMACK = 1
Establish Communication Request
Establish Communication
Request Acknowledge
Until COMMACK=0
S1F13
S1F14
COMMACK = 0
Disable all Events
S2F37
S2F38
Define Reports
S2F33
S2F34
Enable Events
S2F37
S2F38
Data and Time Set Request
S2F31
S2F32
CEED = FALSE
CEED = TRUE
Link Event Reports
S2F35
S2F36
Delete Report Link
S2F35
S2F36
Delete RPTID
S2F33
S2F34
5. SCENARIO
New Equipment Constant
<ECID=101, ECV=‘AP-MR-01’>
S2F15
S2F16
S5F3
S5F4
S5F3
S5F4
ALED = 0 (Disable)
ALED = 1 (Enable)

## Slide 63
■ PAUSE Command (by Host)
5.3 Remote Command Scenario
HOST
TOOL
S2F42
ACK
S6F11
EquipmentStateChanged
< EqpState=4(Down)>
5. SCENARIO
S2F41
Host Command (PAUSE)
S6F12
ACK
■ PAUSE Command (by Equipment)
HOST
TOOL
S6F12
ACK
S6F11
EquipmentStateChanged
< EqpState=4(Down)>

## Slide 64
5. SCENARIO
■ RESUME Command (by Equipment)
HOST
TOOL
S6F12
ACK
■ RESUME Command (by Host)
HOST
TOOL
S2F42
ACK
S2F41
Host Command (RESUME)
S6F12
ACK
S6F11
EquipmentStateChanged
< EqpState =1(Idle) or 2(Run)>
S6F11
EquipmentStateChanged
< EqpState =1(Idle) or 2(Run)>

## Slide 65
5.4 Normal Scenario
HOST
TOOL
5. SCENARIO
IP01에 Tray 투입
Tray 로딩 완료
Tray ID 리딩
Tray Standby(CV Up)
Tray 센터링
작업자가 Tray 장착
S2F41 RCMD=WORK_START
(WORK_ID)
S6F11(1411)
TrayIDRead
(IP01, TrayID)
S6F11(1502)
PortTransferBolcked
(IP01)
S6F11(1401)
TrayLoadComplete
(IP01)
S6F11(1503)
PortReadyToLoad
(IP01)
S3F41
Work Order Request
Tray에서 Glass 배출 시작
TM01(Glass&간지 이재기) 간지 이재
S6F11 (TM01)
ModuleStart (1101)
마지막 Glass까지 작업 반복

## Slide 66
HOST
TOOL
5. SCENARIO
Glass ID 리딩
Glass TM01로 이동
S6F11 (TM01)
SubstrateLocationOccupied (1201)
SubstrateLocationUnoccupied (1202)
ModuleEnd (1102)
Glass BF01로 이동
S6F11 (IP01)
TrayGlassOut (1412)
S6F11
ModuleStart (1101)
SubstrateLocationOccupied (1201)
SubstrateLocationUnoccupied (1202)
ModuleEnd (1102)
S6F11(1601)
GlassIDRead
(TM01, PreviousGlassID, GlassID)
리딩 실패해도 EFEM 반송하고,
GlassID는 Unknown
Glass USC01 로 이동
S6F11
ModuleStart (1101) SubstrateLocationOccupied (1201)
GlassStart (1611)
S6F11
WorkStart (1301)
Tray의 첫 Glass를 TM01 Arm이 흡착
S6F11
ProcessStart (1311)
Tray의 첫 Glass를 TM01 정위치 이동 완료
S6F11
ProcessEnd (1312)
Tray의 마지막 Glass를 TM01 정위치 이동 완료

## Slide 67
HOST
TOOL
5. SCENARIO
USC 작업 완료
S6F11
GlassEnd (1612)
SubstrateLocationUnoccupied (1202)
ModuleEnd (1102)
USC에서 EFEM으로 Glass 배출
Glass EFEM으로 이동
마지막 Glass까지 작업(TRAY->TM01->BF01>USC->EFEM) 반복
S6F11 (IP01)
PortReadyToUnload (1504)
Tray에서 Glass 배출 완료
TM01 공Tray 이재
S6F11 (TM01)
ModuleStart (1101)
S6F11 (OP01)
PortTransferBolcked (1502)
TrayUnloadComplete (1402)
S6F11 (TM01)
ModuleEnd (1102)
S6F11 (IP01)
PortReadyToLoad (1503)

## Slide 68
HOST
TOOL
5. SCENARIO
5.5 Tray Scrap Scenario
S6F11(1401)
TrayLoadComplete
(IP01, TrayID)
Tray 로딩 완료
S2F49 RCMD=TRAY_SCRAP
(TRAYID)
IP01에 Tray 투입
Buzzer 발생하여 작업자가 Tray 제거
S6F11(1403)
TrayScrapComplete
(IP01, TrayID)
Tray ID 리딩
S6F11(1411)
TrayIDRead
(IP01, TrayID)

## Slide 69
HOST
TOOL
5. SCENARIO
5.6 Glass Scrap Scenario
알람 발생
작업자가 Scrap된 Glass를 제거
S6F11(1032)
AlarmCleared
S6F11(1051)
EquipmentStateChanged(Down)
S5F1
AlarmSet
S5F1
AlarmReset
S6F11(1031)
AlarmDetected
S6F11(1602)
GlassScrapComplete(GlassID)