## Slide 1
Version 1.0.2
2023.07
DFR Develop
SECS/GEM Specification

## Slide 2
Revision History
Ver | Date | Chapter | Description
1.0.0 | 2023-04-15 |  | Draft
1.0.1 | 2023-04-24 |  | Control Job, Process Job 삭제
1.0.2 | 2023-07-06 |  | 이벤트 추가 (CEID=1321 GlassScrapComplete)

## Slide 3
CONTENTS
1. DFR DEVELOP Equipment Specifications
2. CEID(Collected Event ID), SVID List
3. SECS-II Message Summary
4. SECS Message Stream & Functions
5. SCENARIO

## Slide 4
1. DFR DEVELOP Equipment Specifications
1.1 Layout

## Slide 5
EQPID | Module | Description | Location ID
AP-TG-05 | In-C/V | EFEM으로부터 받는 투입 C/V | IP01
 | DEVELOP | NT01로부터 받음 | DEV01
 | RINSE 1 | DEV01로부터 받음 | RS01
 | RINSE 2 | RS01로부터 받음 | RS02
 | RINSE 3 | RS02로부터 받음 | RS03
 | RINSE 4 | RS03로부터 받음 | RS04
 | Final RINSE | RS04로부터 받음 | RS05
 | Air Knife | RS05로부터 받음 | AK01
 | Buffer | AK01로부터 받음 | BF01
 | Lifter | BF01로부터 받음 | LF01
 | Upper-C/V | Lifter로부터 받고, 상단 C/V를 거쳐 OP01로 반송 | UCV01~UCV05
 | Out-C/V | UCV01로부터 받고, EFEM으로 배출 C/V | OP01
1.2 Location ID LIST
IP01
DEV01
UCV05
OP01
LF01
BF01
AK01
RS01
RS02
RS03
RS04
RS05
UCV04
UCV03
UCV01
UCV02

## Slide 6
2.1 CEID(Collected Event ID)
CEID | Event | Description
1001 | ControlStateOffline | Equipment control state turn into OFFLINE
1002 | ControlStateLocal | Equipment control state turn into ONLINE LOCAL
1003 | ControlStateRemote | Equipment control state turn into ONLINE REMOTE
1015 | EquipmentConstantChanged | Equipment Constant is changed
1031 | AlarmDetected | alarm occurred
1032 | AlarmCleared | alarm cleared
1051 | EquipmentStateChanged | Equipment State is changed
1061 | OperationIDChanged | Events that occur when worker information registered in the HMI is changed
1101 | ModuleStart | Glass started operating on module
1102 | ModuleEnd | Glass completed operating on module
1201 | SubstrateLocationOccupied | Glass loaded into module
1202 | SubstrateLocationUnoccupied | Glass ejected into module
1301 | GlassStart | First Glass arrived first module
1302 | GlassEnd | Last Glass departed last module
1311 | GlassStartEach | Each Glass arrived first module
1312 | GlassEndEach | Each Glass departed last module
1401 | ProcessData | Glass Process Data
2.1.1 CEID LIST(1)

## Slide 7
2.2 EC(Equipment Constant)
ID | Name | Type | Unit | Min | Max | Def | Description
101 | EqpName | A |  | AP-TG-05 | AP-TG-05 | AP-TG-05 | DFR Develop Equipment Name
102 | SessionID | U2 |  | 0 | 65535 | 0 | HSMS Session ID
103 | HsmsLinkTestInterval | U4 | sec | 10 | 86400 | 120 | HSMS Link Test Period
104 | EstablishCommnucationsTimeout | U4 | sec | 2 | 120 | 10 | Timeout for Establish Commnunication Message
105 | TimeFormat | U4 |  | 0 | 1 | 1 | 0 = 12 bytes format "YYMMDDhhmmss" 1 = 16 bytes format "YYYYMMDDhhmmsscc"
106 | T3TimeOut | U4 | sec | 1 | 120 | 45 | HSMS T3 Time
107 | T5TimeOut | U4 | sec | 1 | 240 | 10 | HSMS T5 Time
108 | T6TimeOut | U4 | sec | 1 | 240 | 5 | HSMS T6 Time
109 | T7TimeOut | U4 | sec | 1 | 240 | 10 | HSMS T7 Time
110 | T8TimeOut | U4 | sec | 1 | 240 | 5 | HSMS T8 Time
111 | UseS6F1Reply | Bo |  | false | true | false | true = need S6F1Reply (S6F2)
2.2.1 EC LIST(1)

## Slide 8
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(1)
ID | Name | TYPE | Description
200 | CommState | U4 | 0 = Undefined 1 = Disabled 2 = Enabled / Not Communicating 3 = Equipment-Initiated Connect / Wait Delay 4 = Equipment-Initiated Connect / Wait CRA 5 = Host-Initiated Connect / Wait CR from Host 6 = Communicating
201 | ControlState | U4 | 1 = Equipment-Offline 2 = Attempt Online 3 = Host Offline 4 = Online-Local 5 = Online-Remote
202 | PreviousControlState | U4 | Previous Control state
203 | EqpState | U4 | 1 = Idle 2 = Run 3 = Maintenance 4 = Down
204 | PreviousEqpState | U4 | Previous Eqp State
205 | UserId | A | userId (current)
206 | PreviousUserId | A | last userid
210 | EventsEnabled | L | L,n n = # of events enabled 1.<CEID_1> … n.<CEID_n>
211 | AlarmsEnabled | L | L,n n = # of alarms enabled 1.<ALID_1> … n.<ALID_n>
212 | AlarmsSet | L | L,n n = # of alarms setted 1.<ALID_1> … n.<ALID_n>
220 | MDLN | A | “DFR” Equipment Model Type. Same data as returned by S1,F2
221 | SOFTREV | A | Software revision code.

## Slide 9
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(2)
ID | Name | TYPE | Description
11001 | PV_MotorSpeed | F4 | Motor Speed 설정
11101 | DEV01_PV_MixingTank_Concentration | F4 | Mixing tank 농도
11102 | DEV01_PV_MixingTank_SupplyFlowRate | F4 | Mixing tank 공급 유량
11103 | DEV01_PV_MixingTank_FlowRate | F4 | Mixing tank 유량
11111 | DEV01_PV_StorageTank_Conductivity | F4 | Storage Tank 전도도
11112 | DEV01_PV_StorageTank_Concentration | F4 | Storage Tank 농도
11113 | DEV01_PV_StorageTank_Temperature | F4 | Storage Tank 온도
11121 | DEV01_PV_Na2CO3Tank_Concentration | F4 | Na2CO3(공급) Tank 농도
11122 | DEV01_PV_Na2CO3Tank_Temperature | F4 | Na2CO3(공급) Tank 온도
11131 | DEV01_PV_DevelopZone_UpPressure | F4 | Develop Zone 상 압력
11132 | DEV01_PV_DevelopZone_DownPressure | F4 | Develop Zone 하 압력
13101 | AK01_PV_Temperature | F4 | A/knife 온도(Hot A/Knife)

## Slide 10
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(3)
ID | Name | TYPE | Description
20101 | IP01_GlassID | A | Glass ID for IP01
20102 | IP01_PPID | A | EFEM PPID for IP01
20103 | IP01_PortID | U2 | EFEM Port ID for IP01
20104 | IP01_CarrierID | A | EFEM Carrier ID for IP01
20105 | IP01_LotID | A | EFEM Lot ID for IP01
20106 | IP01_SlotNo | U2 | EFEM Slot No for IP01
20201 | DEV01_GlassID | A | Glass ID for DEV01
20202 | DEV01_PPID | A | EFEM PPID for DEV01
20203 | DEV01_PortID | U2 | EFEM Port ID for DEV01
20204 | DEV01_CarrierID | A | EFEM Carrier ID for DEV01
20205 | DEV01_LotID | A | EFEM Lot ID for DEV01
20206 | DEV01_SlotNo | U2 | EFEM Slot No for DEV01
20301 | RS01_GlassID | A | Glass ID for RS01
20302 | RS01_PPID | A | EFEM PPID for RS01
20303 | RS01_PortID | U2 | EFEM Port ID for RS01
20304 | RS01_CarrierID | A | EFEM Carrier ID for RS01
20305 | RS01_LotID | A | EFEM Lot ID for RS01
20306 | RS01_SlotNo | U2 | EFEM Slot No for RS01
20401 | RS02_GlassID | A | Glass ID for RS02
20402 | RS02_PPID | A | EFEM PPID for RS02
20403 | RS02_PortID | U2 | EFEM Port ID for RS02
20404 | RS02_CarrierID | A | EFEM Carrier ID for RS02
20405 | RS02_LotID | A | EFEM Lot ID for RS02
20406 | RS02_SlotNo | U2 | EFEM Slot No for RS02

## Slide 11
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(4)
ID | Name | TYPE | Description
20501 | RS03_GlassID | A | Glass ID for RS03
20502 | RS03_PPID | A | EFEM PPID for RS03
20503 | RS03_PortID | U2 | EFEM Port ID for RS03
20504 | RS03_CarrierID | A | EFEM Carrier ID for RS03
20505 | RS03_LotID | A | EFEM Lot ID for RS03
20506 | RS03_SlotNo | U2 | EFEM Slot No for RS03
20601 | RS04_GlassID | A | Glass ID for RS04
20602 | RS04_PPID | A | EFEM PPID for RS04
20603 | RS04_PortID | U2 | EFEM Port ID for RS04
20604 | RS04_CarrierID | A | EFEM Carrier ID for RS04
20605 | RS04_LotID | A | EFEM Lot ID for RS04
20606 | RS04_SlotNo | U2 | EFEM Slot No for RS04
20701 | RS05_GlassID | A | Glass ID for RS05
20702 | RS05_PPID | A | EFEM PPID for RS05
20703 | RS05_PortID | U2 | EFEM Port ID for RS05
20704 | RS05_CarrierID | A | EFEM Carrier ID for RS05
20705 | RS05_LotID | A | EFEM Lot ID for RS05
20706 | RS05_SlotNo | U2 | EFEM Slot No for RS05
20801 | AK01_GlassID | A | Glass ID for AK01
20802 | AK01_PPID | A | EFEM PPID for AK01
20803 | AK01_PortID | U2 | EFEM Port ID for AK01
20804 | AK01_CarrierID | A | EFEM Carrier ID for AK01
20805 | AK01_LotID | A | EFEM Lot ID for AK01
20806 | AK01_SlotNo | U2 | EFEM Slot No for AK01

## Slide 12
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(5)
ID | Name | TYPE | Description
20901 | BF01_GlassID | A | Glass ID for BF01
20902 | BF01_PPID | A | EFEM PPID for BF01
20903 | BF01_PortID | U2 | EFEM Port ID for BF01
20904 | BF01_CarrierID | A | EFEM Carrier ID for BF01
20905 | BF01_LotID | A | EFEM Lot ID for BF01
20906 | BF01_SlotNo | U2 | EFEM Slot No for BF01
21001 | LF01_GlassID | A | Glass ID for LF01
21002 | LF01_PPID | A | EFEM PPID for LF01
21003 | LF01_PortID | U2 | EFEM Port ID for LF01
21004 | LF01_CarrierID | A | EFEM Carrier ID for LF01
21005 | LF01_LotID | A | EFEM Lot ID for LF01
21006 | LF01_SlotNo | U2 | EFEM Slot No for LF01
21101 | UCV01_GlassID | A | Glass ID for UCV01
21102 | UCV01_PPID | A | EFEM PPID for UCV01
21103 | UCV01_PortID | U2 | EFEM Port ID for UCV01
21104 | UCV01_CarrierID | A | EFEM Carrier ID for UCV01
21105 | UCV01_LotID | A | EFEM Lot ID for UCV01
21106 | UCV01_SlotNo | U2 | EFEM Slot No for UCV01
21201 | UCV02_GlassID | A | Glass ID for UCV02
21202 | UCV02_PPID | A | EFEM PPID for UCV02
21203 | UCV02_PortID | U2 | EFEM Port ID for UCV02
21204 | UCV02_CarrierID | A | EFEM Carrier ID for UCV02
21205 | UCV02_LotID | A | EFEM Lot ID for UCV02
21206 | UCV02_SlotNo | U2 | EFEM Slot No for UCV02

## Slide 13
2.3 SVID(State Variable ID)
2.3.1 SVID LIST(6)
ID | Name | TYPE | Description
21301 | UCV03_GlassID | A | Glass ID for UCV03
21302 | UCV03_PPID | A | EFEM PPID for UCV03
21303 | UCV03_PortID | U2 | EFEM Port ID for UCV03
21304 | UCV03_CarrierID | A | EFEM Carrier ID for UCV03
21305 | UCV03_LotID | A | EFEM Lot ID for UCV03
21306 | UCV03_SlotNo | U2 | EFEM Slot No for UCV03
21401 | UCV04_GlassID | A | Glass ID for UCV04
21402 | UCV04_PPID | A | EFEM PPID for UCV04
21403 | UCV04_PortID | U2 | EFEM Port ID for UCV04
21404 | UCV04_CarrierID | A | EFEM Carrier ID for UCV04
21405 | UCV04_LotID | A | EFEM Lot ID for UCV04
21406 | UCV04_SlotNo | U2 | EFEM Slot No for UCV04
21501 | UCV05_GlassID | A | Glass ID for UCV05
21502 | UCV05_PPID | A | EFEM PPID for UCV05
21503 | UCV05_PortID | U2 | EFEM Port ID for UCV05
21504 | UCV05_CarrierID | A | EFEM Carrier ID for UCV05
21505 | UCV05_LotID | A | EFEM Lot ID for UCV05
21506 | UCV05_SlotNo | U2 | EFEM Slot No for UCV05
21601 | OP01_GlassID | A | Glass ID for OP01
21602 | OP01_PPID | A | EFEM PPID for OP01
21603 | OP01_PortID | U2 | EFEM Port ID for OP01
21604 | OP01_CarrierID | A | EFEM Carrier ID for OP01
21605 | OP01_LotID | A | EFEM Lot ID for OP01
21606 | OP01_SlotNo | U2 | EFEM Slot No for OP01

## Slide 14
2.4 Report of Collection Events
2.4.1 DVID LIST(1)
ID | Name | TYPE | Description
301 | ALCD | Bi | Alarm code byte
302 | ALID | U4 | AlarmID of the most recent alarm to change state.
303 | ALTX | A | AlarmText of the most recent alarm to change state
304 | ECID | U4 | Equipment Constant ID
305 | ECNAME | A | Equipment Constant Name
306 | ECV | Any | Equipment Constant Value
307 | PPChangeName | A | 
308 | PPChangeStatus | U2 | 1 = created 2 = edited 3 = deleted
309 | PPCurrentSelected | A | Current selected PPID
310 | ModuleID | A | Substrate Location ID
311 | GlassID | A | Substrate ID
312 | PPID | A | EFEM PPID
313 | PortID | U2 | EFEM PortID
314 | CarrierID | A | EFEM CarrierID
315 | LotID | A | EFEM LotID
316 | SlotNo | U2 | EFEM SlotNo
321 | ProcessDataList | L | L,n n = # of DCOL 1.<DCOL_Value_1> … n.<DCOL_Value_n> ex) AK01 모듈 (DVID = 43101, 43102, 43103) L, 3 <A [3] "1.1"> <A [3] "2.1"> <A [3] "3.1">

## Slide 15
2.4 Report of Collection Events
2.4.1 DVID LIST(2)
ID | Name | TYPE | Description
41101 | DEV01_MotorSpeed | A | Motor Speed
41102 | DEV01_ProcessingTime | A | Processing time for glass.
41103 | DEV01_LiquidTemperature | A | 약액 온도
41104 | DEV01_LiquidFlowRate | A | 약액 유량
41105 | DEV01_LiquidConcentration | A | 약액 농도
41106 | DEV01_AquaNozzlePressureData | A | Aqua Knife 압력 Data
41107 | DEV01_UpperNozzlePressureData | A | 상부 Nozzle 압력 Data
41108 | DEV01_LowerNozzlePressureData | A | 하부 Nozzle 압력 Data
41109 | DEV01_OutputAirCurtainUpperNozzlePressureData | A | Out A/curtain 상부 Nozzle 압력 Data
41110 | DEV01_OutputAirCurtainLowerNozzlePressureData | A | Out A/curtain 하부 Nozzle 압력 Data

## Slide 16
2.4 Report of Collection Events
2.4.1 DVID LIST(4)
ID | Name | TYPE | Description
42101 | RS01_MotorSpeed | A | Motor Speed
42102 | RS01_ProcessingTime | A | Processing time for glass.
42103 | RS01_UpperNozzlePressureData | A | Rinse #1 압력 Data 상부 nozzle
42104 | RS01_LowerNozzlePressureData | A | Rinse #1 압력 Data 하부 nozzle

## Slide 17
2.4 Report of Collection Events
2.4.1 DVID LIST(5)
ID | Name | TYPE | Description
42201 | RS02_MotorSpeed | A | Motor Speed
42202 | RS02_ProcessingTime | A | Processing time for glass.
42203 | RS02_UpperNozzlePressureData | A | Rinse #2 압력 Data 상부 nozzle
42204 | RS02_LowerNozzlePressureData | A | Rinse #2 압력 Data 하부 nozzle

## Slide 18
2.4 Report of Collection Events
2.4.1 DVID LIST(6)
ID | Name | TYPE | Description
42301 | RS03_MotorSpeed | A | Motor Speed
42302 | RS03_ProcessingTime | A | Processing time for glass.
42303 | RS03_UpperNozzlePressureData | A | Rinse #3 압력 Data 상부 nozzle
42304 | RS03_LowerNozzlePressureData | A | Rinse #3 압력 Data 하부 nozzle

## Slide 19
2.4 Report of Collection Events
2.4.1 DVID LIST(7)
ID | Name | TYPE | Description
42401 | RS04_MotorSpeed | A | Motor Speed
42402 | RS04_ProcessingTime | A | Processing time for glass.
42403 | RS04_UpperNozzlePressureData | A | Rinse #4 압력 Data 상부 nozzle
42404 | RS04_LowerNozzlePressureData | A | Rinse #4 압력 Data 하부 nozzle

## Slide 20
2.4 Report of Collection Events
2.4.1 DVID LIST(8)
ID | Name | TYPE | Description
42501 | RS05_MotorSpeed | A | Motor Speed
42502 | RS05_ProcessingTime | A | Processing time for glass.
42503 | RS05_UpperNozzlePressureData | A | Rinse #5 압력 Data 상부 nozzle
42504 | RS05_LowerNozzlePressureData | A | Rinse #5 압력 Data 하부 nozzle

## Slide 21
2.4 Report of Collection Events
2.4.1 DVID LIST(9)
ID | Name | TYPE | Description
43101 | AK01_MotorSpeed | A | Motor Speed
43102 | AK01_ProcessingTime | A | Processing time for glass.
43103 | AK01_Temperature | A | A/Knife(Hot Air) 온도

## Slide 22
2.5 Report of Collection Events
2.5.1 RPTID/CEID/VID List(1)
CEID | RPTID | VID | Contents
1001 1002 1003 |  |  | ControlStateOffline
 |  |  | ControlStateLocal
 |  |  | ControlStateRemote
 | 101 | 201 | ControlState
 |  | 202 | PreviousControlState
1015 |  |  | EquipmentConstantChanged
 | 102 | 304 | ECID
 |  | 305 | ECNAME
 |  | 306 | ECV
1031 1032 |  |  | AlarmDected
 |  |  | AlarmCleared
 | 103 | 310 | ModuleID
 |  | 301 | ALCD
 |  | 302 | ALID
 |  | 303 | ALTX
1051 |  |  | EquipmentStateChanged
 | 104 | 203 | EqpState
 |  | 204 | PreviousEqpState
1061 |  |  | OperationIDChanged
 | 105 | 205 | UserId
 |  | 206 | PreviousUserId
1071 |  |  | PPChanged
 | 106 | 307 | PPChangeName
 |  | 308 | PPChangeStatus
1072 |  |  | PPSelected
 | 107 | 309 | PPCurrentSelected

## Slide 23
2.5 Report of Collection Events
2.5.1 RPTID/CEID/VID List(2)
CEID | RPTID | VID | Contents
1101 1102 |  |  | ModuleStart
 |  |  | ModuleEnd
 | 108 | 310 | ModuleID
1201 1202 |  |  | SubstrateLocationOccupied
 |  |  | SubstrateLocationUnoccupied
 | 109 | 310 | ModuleID
 |  | 311 | GlassID
1301 1302 1311 1312 |  |  | GlassStart
 |  |  | GlassEnd
 |  |  | GlassStartEach
 |  |  | GlassEndEach
 | 110 | 310 | ModuleID
 |  | 311 | GlassID
 |  | 312 | PPID
 |  | 313 | PortID
 |  | 314 | CarrierID
 |  | 315 | LotID
 |  | 316 | SlotNo
1321 |  |  | GlassScrap
 | 111 | 310 | ModuleID
 |  | 311 | GlassID
1401 |  |  | ProcessData
 | 112 | 310 | ModuleID
 |  | 311 | GlassID
 |  | 312 | PPID
 |  | 313 | PortID
 |  | 314 | CarrierID
 |  | 315 | LotID
 |  | 316 | SlotNo
 |  | 321 | ProcessDataList

## Slide 24
3. SECS-II Message Summary
Message | Direction | Description | Note
S*F0 | Host ↔ EQ | Abort Transaction | 
S1F1 | Host ↔ EQ | Are You There Request(R) | 
S1F2 | Host ↔ EQ | On-Line Data(D) | 
S1F3 | Host → EQ | Selected equipment status request | 
S1F4 | Host ← EQ | Selected Equipment status Data | 
S1F11 | Host → EQ | Status variable name-list request | 
S1F12 | Host ← EQ | Status Variable name-list reply | 
S1F13 | Host ↔ EQ | Establish communication request | 
S1F14 | Host ↔ EQ | Establish communication request Ack | 
S1F15 | Host → EQ | Request Off-line | 
S1F16 | Host ← EQ | Request Off-line Acknowledge | 
S1F17 | Host → EQ | Request On-line | 
S1F18 | Host ← EQ | Request On-line Acknowledge | 
S2F13 | Host → EQ | Equipment constant request | 
S2F14 | Host ← EQ | Equipment constant data | 
S2F15 | Host → EQ | New equipment constant send | 
S2F16 | Host ← EQ | New equipment constant Ack | 
S2F17 | Host ↔ EQ | Date and time request | 
S2F18 | Host ↔ EQ | Date and time data | 
S2F23 | Host → EQ | Trace Initialize Send | 
S2F24 | Host ← EQ | Trace Initialize Acknowledge | 
S2F25 | Host → EQ | Loop-back diagnostic request | 
S2F26 | Host ← EQ | Loopback Diagnostic Data | 
S2F29 | Host → EQ | Equipment constant name-list request | 
S2F30 | Host ← EQ | Equipment Constant Name-list | 
S2F31 | Host → EQ | Date and time send | 
S2F32 | Host ← EQ | Data and Time Set Acknowledge | 

## Slide 25
3. SECS-II Message Summary
Message | Direction | Description | Note
S2F33 | Host → EQ | Define Report | 
S2F34 | Host ← EQ | Define Report Acknowledge | 
S2F35 | Host → EQ | Link event report | 
S2F36 | Host ← EQ | Link event report acknowledge | 
S2F37 | Host → EQ | Enable/disable event report | 
S2F38 | Host ← EQ | Enable/disable event report acknowledge | 
S2F41 | Host → EQ | Host command send | 
S2F42 | Host ← EQ | Host command acknowledge | 
S5F1 | Host ← EQ | Alarm report send | 
S5F2 | Host → EQ | Alarm report send acknowledge | 
S5F3 | Host → EQ | Enable/disable alarm send | 
S5F4 | Host ← EQ | Enable/disable alarm acknowledge | 
S5F5 | Host → EQ | List alarms request | 
S5F6 | Host ← EQ | List alarms data | 
S5F7 | Host → EQ | List enabled alarm request | 
S5F8 | Host ← EQ | List enabled alarm data | 
S6F1 | Host ← EQ | Trace Data Send | 
S6F2 | Host → EQ | Trace Data Acknowledge | 
S6F11 | Host ← EQ | Event report send | 
S6F12 | Host → EQ | Event report acknowledge | 
S7F1 | Host ↔ EQ | Process Program Load Inquire | 
S7F2 | Host ↔ EQ | Process Program Load Grant | 
S7F17 | Host → EQ | Delete Process Program Send | 
S7F18 | Host ← EQ | Delete Process Program Acknowledge | 
S7F19 | Host → EQ | Current EPPD Request | 
S7F20 | Host ← EQ | Current EPPD Data | 

## Slide 26
3. SECS-II Message Summary
Message | Direction | Description | Note
S7F23 | H ↔ E | Formatted Process Program Send | 
S7F24 | H ↔ E | Formatted Process Program Acknowledge | 
S7F25 | H ↔ E | Formatted Process Program Request | 
S7F26 | H ↔ E | Formatted Process Program Data | 
S9F1 | Host ← EQ | Unrecognized device ID | 
S9F3 | Host ← EQ | Unrecognized stream type | 
S9F5 | Host ← EQ | Unrecognized function type | 
S9F7 | Host ← EQ | Illegal data | 
S9F9 | Host ← EQ | Transaction timer timeout | 
S9F11 | Host ← EQ | Data too long | 
S10F3 | H → E | Terminal displaysingle | 
S10F4 | H ← E | Terminal displaysingle acknowledge | 

## Slide 27
4. SECS Message Stream & Functions
4.1 Operational Concept
4.1.1 Data Format Length
I1 - Integer 1 Byte : From _128 to +127
I2 - Integer 2 Bytes : From _32,768 to +32,768
I4 - Integer 4 Bytes : From _2,157,483,648 to +2,157,483,648
I8 - Integer 8 Bytes : From _9,223,372,036,854,775,808 to +9,223,372,036,854,775,808
U1 - Unsigned 1 Bytes : From 0 to 255
U2 - Unsigned 2 Bytes : From 0 to 65,535
U4 - Unsigned 4 Bytes : From 0 to 4,294,967,295
U8 - Unsigned 8 Bytes : From 0 to 18,446,744,073,709,551,615
F4 - 4-byte floating point : From -3.40282347E+38F to 3.40282347E+38F
F8 - 8-byte floating point : From -1.7976931348623157E+308 to 1.7976931348623157E+308
Boolean : "False" or “True"
A[자릿수] - ASCII : Ex) a~z, A~Z, 0~9, _, space, (, ), etc

## Slide 28
4. SECS Message Stream & Functions
4.2 STREAM 1
■ S1, F2 On-line Data (H ← E) |  |  | 
 | Structure |  | 
 | L , 2 1. <A MDLN> 2. <A SOFTREV> |  | 
 | Dictionary |  | 
 | MDLN | Equipment ModelType, 6bytes max | Same data as returned by S1, F2
 | SOFTREV | Software revision code 6 bytes maximum | 
■ S1, F2 On-line Data (H → E) | 
 | Structure
 | L , 0
■ S1, F1 Are You There Request (H ↔ E) | 
 | Description
 | Establishes that the SECS-II link is operational and that the host and machine are online. The machine responds with its model number and software revision. The host responds with a null list. The equipment may use this message when using SECS-I as a "heartbeat" to detect communication failures. The equipment also uses this message in the Control State model when attempting to go online
 | Structure
 | Header only
■ S1, F3 Selected Equipment Status Request (H → E) |  |  | 
 | Structure |  | 
 | L , n 1. <U4 SVID> … n. <U4 SVID> |  | 
 | Dictionary |  | 
 | SVID | Status variable ID | Status variables may include any parameter that can be sampled in time such as temperature or quantity of a consumable.

## Slide 29
■ S1, F4 Selected Equipment Status Data(H ← E) |  |  | 
 | Structure |  | 
 | L , n 1. <* SV> n. <* SV> |  | 
 | Note |  | 
 | A zero-length U1 for SV means that the SVID does not exist. |  | 
 | Dictionary |  | 
 | SV | Status variable value | 
■ S1, F11 Status Variable Namelist Request ( (H → E) |  |  | 
 | Description |  | 
 | A request from the host to the machine to report the name and units of certain status variables, in the order requested. |  | 
 | Structure |  | 
 | L , n 1. <U4 SVID> … n. <U4 SVID> |  | 
 | Dictionary |  | 
 | SVID | Status variable ID | Status variables may include any parameter that can be sampled in time such as temperature or quantity of a consumable.
4. SECS Message Stream & Functions

## Slide 30
■ S1, F13 Establish Communications Request(H ↔ E) | 
 | Structure
 | L , 0
■ S1, F14 Establish Communications Request Acknowledge(H ↔ E) |  |  | 
 | Structure |  | 
 | L , 2 1. <Bi COMMACK> 2. L , 0 |  | 
 | Dictionary |  | 
 | COMMACK | Establish Communications Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied, Try Again 2-63 Reserved
■ S1, F12 Status Variable Namelist Reply(H ← E) |  |  | 
 | Structure |  | 
 | L , n 1. L , 3 1. <U4 SVID> 2. <A SVNAME> 3. <A UNITS> … n. L , 3 1. <U4 SVID> 2. <A SVNAME> 3. <A UNITS> |  | 
 | Dictionary |  | 
 | SVID | Status variable ID | Status variables may include any parameter that can be sampled in time such as temperature or quantity of a consumable.
 | SVNAME | Status Variable Name | 
 | UNITS | Units Identifier | As allowed by SEMI E5 Section 12.
4. SECS Message Stream & Functions

## Slide 31
■ S1, F14 Establish Communications Request Acknowledge(H ↔ E) |  |  | 
 | Structure |  | 
 | L , 2 1. <Bi COMMACK> 2. L , 2 1. <A MDLN> 2. <A SOFTREV> |  | 
 | Dictionary |  | 
 | COMMACK | Establish Communications Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied, Try Again 2-63 Reserved
 | MDLN | Equipment ModelType, 6bytes max | Same data as returned by S1, F2
 | SOFTREV | Software revision code 6 bytes maximum | 
■ S1, F13 Establish Communications Request(H ↔ E) |  |  | 
 | Description |  | 
 | Initiate an attempt to establish a SECS-II communications link at a logical level on power-up or after a break in the link. It is the first message sent after either of the above conditions. If no response is received from the host, the machine will periodically send a S1F13 message until a S1F14 with the correct COMMACK is received. |  | 
 | Structure |  | 
 | L , 2 1. <A MDLN> 2. <A SOFTREV> |  | 
 | Dictionary |  | 
 | MDLN | Equipment ModelType, 6bytes max | Same data as returned by S1, F2
 | SOFTREV | Software revision code 6 bytes maximum | 
4. SECS Message Stream & Functions

## Slide 32
■ S1, F18 On-line Control State Acknowledge(H ← E) |  |  | 
 | Structure |  | 
 | 1. <Bi OFLACK> |  | 
 | Dictionary |  | 
 | COMMACK | Establish Communications Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied, Try Again 2-63 Reserved
■ S1, F17 On-line Control State Request(H → E) | 
 | Description
 | The host requests that the equipment transition to the ON-LINE state.
 | Structure
 | Header only
■ S1, F16 Off-line Control State Acknowledge(H ← E) |  |  | 
 | Structure |  | 
 | 1. <Bi OFLACK> |  | 
 | Dictionary |  | 
 | COMMACK | Establish Communications Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied, Try Again 2-63 Reserved
■ S1, F15 Off-line Control State Request(H → E) | 
 | Description
 | The host requests that the equipment transition to the OFF-LINE state.
 | Structure
 | Header only
4. SECS Message Stream & Functions

## Slide 33
4.3 STREAM 2
■ S2, F13 Equipment Constant Request (H → E) |  |  | 
 | Description |  | 
 | A request from the host to report the value of certain equipment constants in a predefined order. |  | 
 | Structure |  | 
 | L , N 1. <U4 ECID> … n. <U4 ECID> |  | 
 | Dictionary |  | 
 | ECID | Equipment Constant ID | 
■ S2, F14 Equipment Constant Data(H ← E) |  |  | 
 | Structure |  | 
 | L , N 1. <* ECV> … n. <* ECV> |  | 
 | Dictionary |  | 
 | ECV | Equipment Constant Value | 
■ S2, F15 New Equipment Constant Send (H → E) |  |  | 
 | Description |  | 
 | Host updates the values of specified EC. If the host returns a non-zero EAC the equipment will not change the value of any ECID specified in the S2F15 body. |  | 
 | Structure |  | 
 | L , n 2. L , 2 <U4 ECID> <* ECV> … n. L , 2 <U4 ECID> <* ECV> |  | 
 | Dictionary |  | 
 | ECID | Equipment Constant ID | 
 | ECV | Equipment Constant Value | 
4. SECS Message Stream & Functions

## Slide 34
■ S2, F17 Date and Time Request (H ↔ E) | 
 | Description
 | The host requests that the equipment transition to the OFF-LINE state.
 | Structure
 | Header only
■ S2, F16 New Equipment Constant Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi EAC> |  | 
 | Dictionary |  | 
 | EAC | Equipment acknowledge code, 1 byte | 0 = Acknowledge 1 = Denied. At least one constant does not exist 2 = Denied. Busy 3 = Denied. At least one constant out of range >3 = Other equipment-specific error 4-63 Reserved
■ S2, F18 Date and Time Data (H ↔ E) |  |  | 
 | Structure |  | 
 | <A TIME> |  | 
 | Note |  | 
 | A zero-length item means no time exists. |  | 
 | Dictionary |  | 
 | TIME | Time of day, 12 or 16 bytes NOTE 4: The 16-byte format is currently optional. After January 1, 1998, the 16-byte format shall be required on new and updated implementations. Support for the 12-byte format shall be supported as a configurable option using the equipment constant TimeFormat. This is a format requirement only and does not imply either precision or accuracy. | If 12 bytes the format is YYMMDDhhmmss YY = Year 00 to 99 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 If 16 bytes the format is YYYYMMDDhhmmsscc YYYY = Year 0000 to 9999 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 cc = Centisecond 00 to 99
4. SECS Message Stream & Functions

## Slide 35
■ S2, F24 Trace Initialize Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi TIAACK> |  | 
 | Dictionary |  | 
 | TIAACK | Equipment acknowledgement code, 1 byte | 0 = Everything correct 1 = Too many SVIDs 2 = No more traces allowed 3 = Invalid period >3 = Equipment-specified error 4-63 Reserved
■ S2, F23 Trace Initialize Send (H → E) |  |  | 
 | Description |  | 
 | The host requests a time driven trace of specified status variables. If TOTSMP is zero, the machine will cancel an existing trace with the given TRID. |  | 
 | Structure |  | 
 | L , 5 1. <U4 TRID> 2. <A DSPER> 3. <U4 TOTSMP> 4. <U4 REPGSZ> 5. L , N 1. <U4 SVID> … 1. <U4 SVID> |  | 
 | Dictionary |  | 
 | TRID | Trace request ID | 
 | DSPER | Data sample period. DSPER has two allowable formats: | Format 1: hhmmss, 6 bytes Format 2: hhmmsscc, 8 bytes Where “hh” is hours, “mm” is minutes, “ss” is seconds’ and “cc” is centiseconds. Equipment shall either (1) support only Format 1, or (2) support both Format 1 and Format 2. Equipment shall document which formats it accepts. Equipment which supports Format 2 need not necessarily support a minimum DSPER of 1 centisecond, nor a trace resolution of 1 centisecond, but equipment suppliers shall document its trace performance limits.
 | TOTSMP | Total samples to be made | 
 | REPGSZ | Reporting group size | 
 | SVID | Status variable ID | Status variables may include any parameter that can be sampled in time such as temperature or quantity of a consumable.
4. SECS Message Stream & Functions

## Slide 36
■ S2, F26 Loop-back Diagnostic Data (H ↔ E) |  |  | 
 | Structure |  | 
 | <** ABS> |  | 
 | Dictionary |  | 
 | ABS | Any binary string | 
■ S2, F29 Equipment Constant Name list Request (H → E) |  |  | 
 | Description |  | 
 | A request from the host to the equipment to retrieve information regarding the specified equipment constants. A zero length list (n = 0) means to send information for all ECID. |  | 
 | Structure |  | 
 | L , n 1. <U4 ECID> … n. <U4 ECID> |  | 
 | Dictionary |  | 
 | ECID | Equipment Constant ID | 
■ S2, F25 Loop-back Diagnostic Request (H ↔ E) |  |  | 
 | Description |  | 
 | A diagnostic message for checkout of protocol and communication circuits. The message sent is echoed back. |  | 
 | Structure |  | 
 | <* ABS> |  | 
 | Dictionary |  | 
 | ABS | Any binary string | 
4. SECS Message Stream & Functions

## Slide 37
■ S2, F30 Equipment Constant Name list (H ← E) |  |  | 
 | Structure |  | 
 | L , n 1. L , 6 1. <U4 ECID> 2. <A ECNAME> 3. <* ECMIN> 4. <* ECMAX> 5. <* ECDEF> 6. <A UNITS> … n. L , 6 1. <U4 ECID> 2. <A ECNAME> 3. <* ECMIN> 4. <* ECMAX> 5. <* ECDEF> 6. <A UNITS> |  | 
 | Note |  | 
 | Zero length ASCII items for ECNAME, ECMIN, ECMAX, ECDEF and UNITS indicates that the ECID does not exist. |  | 
 | Dictionary |  | 
 | ECID | Equipment Constant ID | 
 | ECNAME | Equipment constant name | 
 | ECMIN | Equipment constant minimum value | 
 | ECMAX | Equipment constant maximum value | 
 | ECDEF | Equipment constant default value | 
 | UNITS | Units Identifier | As allowed by SEMI E5 Section 12.
4. SECS Message Stream & Functions

## Slide 38
■ S2, F31 Date and Time Set Request (H → E) |  |  | 
 | Description |  | 
 | The host instructs the equipment to set its time base to the specified value. |  | 
 | Structure |  | 
 | <A TIME> |  | 
 | Dictionary |  | 
 | TIME | Time of day, 12 or 16 bytes NOTE 4: The 16-byte format is currently optional. After January 1, 1998, the 16-byte format shall be required on new and updated implementations. Support for the 12-byte format shall be supported as a configurable option using the equipment constant TimeFormat. This is a format requirement only and does not imply either precision or accuracy. | If 12 bytes the format is YYMMDDhhmmss YY = Year 00 to 99 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 If 16 bytes the format is YYYYMMDDhhmmsscc YYYY = Year 0000 to 9999 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 cc = Centisecond 00 to 99
■ S2,F32 Date and Time Set Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi TIACK> |  | 
 | Dictionary |  | 
 | TIAACK | Equipment acknowledgement code, 1 byte | 0 = Everything correct 1 = Too many SVIDs 2 = No more traces allowed 3 = Invalid period >3 = Equipment-specified error 4-63 Reserved
4. SECS Message Stream & Functions

## Slide 39
■ S2, F33 Define Report (H → E) |  |  | 
 | Structure |  | 
 | L , 2 1. <U4 DATAID> 2. L , a 1. L , 2 1. <U4 RPTID> 2. L , b 1. <U4 VID> … b. <U4 VID> … a. L , 2 1. <U4 RPTID> 2. L , c 1. <U4 VID> … c. <U4 VID> |  | 
 | Note |  | 
 | A zero-length list following DATAID deletes all report definitions and associated links. See S2, F35. A zero-length list following RPTID deletes report type RPTID. All CEID links to this RPTID are also deleted. |  | 
 | Dictionary |  | 
 | DATAID | Data ID | 
 | RPTID | Report ID | 
 | VID | Variable ID | 
■ S2, F34 Define Report Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi DRACK> |  | 
 | Dictionary |  | 
 | DRACK | Define Report Acknowledge Code, 1 byte | 0 = Accept 1 = Denied. Insufficient space 2 = Denied. Invalid format 3 = Denied. At least one RPTID already defined 4 = Denied. At least VID does not exist >4 = Other errors 5-63 Reserved
4. SECS Message Stream & Functions

## Slide 40
■ S2, F35 Link Event Report (H → E) |  |  | 
 | Description |  | 
 | The host links Report IDs (RPTID) to Collection event IDs (CEID). These linked event reports default to "disabled" upon linking. That is, the occurrence of an event would not cause the report to be sent until enabled. See S2, F37 for enabling events. |  | 
 | Structure |  | 
 | L , 2 1. <U4 DATAID> 2. L , a 1. L , 2 1. <U4 CEID> 2. L , b 1. <U4 RPTID> … b. <U4 RPTID> … a. L , 2 1. <U4 CEID> 2. L , c 1. <U4 RPTID> … c. <U4 RPTID> |  | 
 | Note |  | 
 | A zero-length list following CEID deletes all report links to that event. |  | 
 | Dictionary |  | 
 | DATAID | Data ID | 
 | CEID | Collected event ID | 
 | RPTID | Report ID | 
■ S2, F36 Link Event Report Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi DRACK> |  | 
 | Dictionary |  | 
 | DRACK | Define Report Acknowledge Code, 1 byte | 0 = Accept 1 = Denied. Insufficient space 2 = Denied. Invalid format 3 = Denied. At least one RPTID already defined 4 = Denied. At least VID does not exist >4 = Other errors 5-63 Reserved
4. SECS Message Stream & Functions

## Slide 41
■ S2, F37 Enable/Disable Event Report (H → E) |  |  | 
 | Description |  | 
 | Host requests to enable or disable reporting for a list of Collection events (CEID). |  | 
 | Structure |  | 
 | L , 2 1. <Bo CEED> 2. L , n 1. <U4 CEID> … n. <U4 CEID> |  | 
 | Note |  | 
 | A zero-length list (n = 0) means all CEID. |  | 
 | Dictionary |  | 
 | CEED | Collection event or trace enable/disable code, 1 byte | FALSE = Disable TRUE = Enable
 | CEID | Collected event ID | 
■ S2, F38 Enable/Disable Event Report Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi ERACK> |  | 
 | Dictionary |  | 
 | ERACK | Enable/Disable Event Report Acknowledge Code, 1 byte | 0 = Accepted 1 = Denied. At least one CEID does not exist >1 = Other Errors 2-63 Reserved
4. SECS Message Stream & Functions

## Slide 42
■ S2, F41 Host Command Send(H → E) |  |  | 
 | Description |  | 
 | The host sends a request to the equipment to perform the specified command with the relevant parameters. |  | 
 | Structure |  | 
 | L 2 1. <A RCMD> 2. L , 1 1. L , 2 1. <A CPNAME> 2. <A CPVAL> |  | 
 | Dictionary |  | 
 | RCMD | Remote command code or string | 
 | CPNAME | Parameter name | 
 | CPVAL | Command Parameter Value. | 
4. SECS Message Stream & Functions

## Slide 43
■ S2, F42 Host Command Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | L , 2 1. <Bi HCACK> 2. L , n 1. L , 2 1. <A CPNAME> 2. <* CEPACK> … n. L , 2 1. <A CPNAME> 2. <* CEPACK> |  | 
 | Dictionary |  | 
 | HCACK | Host Command Parameter Acknowledge Code, 1 byte | 0 = Acknowledge, command has been performed 1 = Command does not exist 2 = Cannot perform now 3 = At least one parameter is invalid 4 = Acknowledge, command will be performed with completion signaled later by an event 5 = Rejected, Already in Desired Condition 6 = No such object exists 7-63 Reserved
 | CPNAME | Recipe name | 
 | CEPACK | Command Enhanced Parameter cknowledge. If a specific value of CPNAME is defined to have a CEPVAL that is a LIST, then CEPACK shall have the same structure as the corresponding list format of CEPVAL as used in S2,F49. Otherwise CEPACK will be a 1 byte integer. Enumerated: | 0 = No error 1 = Parameter name (CPNAME) does not exist 2 = Illegal value specified for CEPVAL 3 = Illegal format specified for CEPVAL 4 = Parameter name (CPNAME) not valid as used 5-63 Reserved
4. SECS Message Stream & Functions

## Slide 44
4.4 STREAM 5
■ S5, F1 Alarm Report Send (H ← E) |  |  | 
 | Description |  | 
 | This message is sent whenever an alarm changes states to "Set" or "Clear" |  | 
 | Structure |  | 
 | L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> |  | 
 | Dictionary |  | 
 | ALCD | Alarm code byte | bit 8 = 1 means alarm set bit 8 = 0 means alarm cleared bit 7-1 is alarm category 0 = Not used 1 = Personal safety 2 = Equipment safety 3 = Parameter control warning 4 = Parameter control error 5 = Irrecoverable error 6 = Equipment status warning 7 = Attention flags 8 = Data integrity >8 = Other categories
 | ALID | Alarm identification | 
 | ALTX | Alarm text limited to 40 characters | 
■ S5, F2 Alarm Report Acknowledge (H → E) |  |  | 
 | Structure |  | 
 | <Bi ACKC5> |  | 
 | Dictionary |  | 
 | ACKC5 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved
4. SECS Message Stream & Functions

## Slide 45
■ S5, F3 Enable/Disable Alarm Send (H → E) |  |  | 
 | Description |  | 
 | This message enables or disables an alarm from being reported to the host. Some alarms (safety related) are not controllable in this way. |  | 
 | Structure |  | 
 | L , 2 1. <Bi ALED> 2. <U4 ALID> |  | 
 | Dictionary |  | 
 | ALED | Alarm enable/disable code, 1 byte | bit 8 = 1 means enable alarm bit 8 = 0 means disable alarm
 | ALID | Alarm identification | 
■ S5, F4 Enable/Disable Alarm Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi ACKC5> |  | 
 | Dictionary |  | 
 | ACKC5 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved
4. SECS Message Stream & Functions

## Slide 46
■ S5, F5 List Alarms Request (H → E) |  |  | 
 | Description |  | 
 | The host requests the equipment to send information on currently defined alarms. |  | 
 | Structure |  | 
 | <U4 ALID1, . . ., ALIDn> |  | 
 | Note |  | 
 | A zero-length item (n = 0) means send all possible alarms regardless of the state of ALED. |  | 
 | Dictionary |  | 
 | ALID | Alarm identification | 
■ S5, F6 List Alarms Data (H ← E) |  |  | 
 | Structure |  | 
 | L , m 1. L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> … m. L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> |  | 
 | Note |  | 
 | If m = 0, no response can be made. A zero-length item returned for ALCD or ALTX means that value does not exist. |  | 
 | Dictionary |  | 
 | ALCD | Alarm code byte | bit 8 = 1 means alarm set bit 8 = 0 means alarm cleared bit 7-1 is alarm category 0 = Not used 1 = Personal safety 2 = Equipment safety 3 = Parameter control warning 4 = Parameter control error 5 = Irrecoverable error 6 = Equipment status warning 7 = Attention flags 8 = Data integrity >8 = Other categories
 | ALID | Alarm identification | 
 | ALTX | Alarm text limited to 40 characters | 
4. SECS Message Stream & Functions

## Slide 47
■ S5, F7 List Alarms Request (H → E) | 
 | Description
 | List alarms which are enabled.
 | Structure
 | Header only
■ S5, F8 List Alarms Data (H ← E) |  |  | 
 | Structure |  | 
 | L , m 1. L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> … m. L , 3 1. <Bi ALCD> 2. <U4 ALID> 3. <A ALTX> |  | 
 | Note |  | 
 | If m = 0, no response can be made. A zero-length item returned for ALCD or ALTX means that value does not exist. |  | 
 | Dictionary |  | 
 | ALCD | Alarm code byte | bit 8 = 1 means alarm set bit 8 = 0 means alarm cleared bit 7-1 is alarm category 0 = Not used 1 = Personal safety 2 = Equipment safety 3 = Parameter control warning 4 = Parameter control error 5 = Irrecoverable error 6 = Equipment status warning 7 = Attention flags 8 = Data integrity >8 = Other categories
 | ALID | Alarm identification | 
 | ALTX | Alarm text limited to 40 characters | 
4. SECS Message Stream & Functions

## Slide 48
4.5 STREAM 6
4. SECS Message Stream & Functions
■ S6, F1 Trace Data Send (H ← E) |  |  | 
 | Description |  | 
 | Trace Samples configured with S2, F23 messages are sent to the host in these messages. |  | 
 | Structure |  | 
 | L , 4 1. <U4 TRID> 2. <U4 SMPLN> 3. <A STIME> L, n 1. <* SV> … n. <* SV> |  | 
 | Dictionary |  | 
 | TRID | Trace request ID | 
 | SMPLN | Sample number | 
 | STIME | Sample time, 12 or 16 bytes. NOTE 3: The 16-byte format is currently optional. After January 1, 1998, the 16-byte format shall be required on new and updated implementations. Support for the 12-byte format shall be supported as a onfigurable option using the equipment constant TimeFormat. This is a format requirement only and does not imply either precision or accuracy. | If 12 bytes the format is YYMMDDhhmmss YY = Year 00 to 99 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 If 16 bytes the format is YYYYMMDDhhmmsscc YYYY = Year 0000 to 9999 MM = Month 01 to 12 DD = Day 01 to 31 hh = Hour 00 to 23 mm = Minute 00 to 59 ss = Second 00 to 59 cc = Centisecond 00 to 99
 | SV | Status variable value | 
■ S6, F2 Trace Data Acknowledge (H → E) |  |  | 
 | Structure |  | 
 | <Bi ACKC6> |  | 
 | Dictionary |  | 
 | ACKC6 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved

## Slide 49
■ S6, F11 Event Report Send (H ← E) |  |  | 
 | Description |  | 
 | The machine sends a defined, event linked and enabled group of reports to the host on a linked event. This is a message that possibly requires a preceding S6, F5/F6 multiblock enquire/grant transaction. |  | 
 | Structure |  | 
 | L , 3 1. <U4 DATAID> 2. <U4 CEID> 3. L , a 1. L , 2 1. <U4 RPTID> 2. L , b 1. <*V> … b. <*V> … a. L , 2 1. <U4 RPTID> 2. L , c 1. <*V> … c. <*V> |  | 
 | Note |  | 
 | If there are no reports linked to the event a "null" report is assumed. A zero-length list for # of reports (a = 0) means there are no reports linked to the given CEID. |  | 
 | Dictionary |  | 
 | DATAID | Data ID | 
 | CEID | Collected event ID | 
 | RPTID | Report ID | 
 | V | Variable data | 
■ S6, F12 Event Report Acknowledge (H → E) |  |  | 
 | Structure |  | 
 | <Bi ACKC6> |  | 
 | Dictionary |  | 
 | ACKC6 | Acknowledge code, 1 byte | 0 = Accepted >0 = Error, not accepted 1-63 Reserved
4. SECS Message Stream & Functions

## Slide 50
4.6 STREAM 7
4. SECS Message Stream & Functions
■ S7, F1 Process Program Load Inquire (H ↔ E) |  |  | 
 | Description |  | 
 | This message is used to initiate the transfer of a process program or to select from stored programs. |  | 
 | Structure |  | 
 | L,2 1. <PPID> 2. <LENGTH> |  | 
 | Dictionary |  | 
 | PPID | Process program ID | Limited to a maximum of 80 bytes.
 | LENGTH | Length of the service program or process program in bytes | 
■ S7, F2 Process Program Load Grant (H ↔ E) |  |  | 
 | Structure |  | 
 | <PPGNT> |  | 
 | Dictionary |  | 
 | PPGNT | Process program grant status, 1 byte | 0 = OK 1 = Already have 2 = No space 3 = Invalid PPID 4 = Busy, try later 5 = Will not accept >5 = Other error 6-63 Reserved
■ S7, F17 Delete Process Program Send (H → E) |  |  | 
 | Description |  | 
 | This message is used by the host to request the equipment to delete process programs from equipment storage. |  | 
 | Structure |  | 
 | L,n (Number of process programs to be deleted) 1. <PPID1> . . n. <PPIDn> |  | 
 | Note |  | 
 | If n = 0, then delete all. |  | 
 | Dictionary |  | 
 | PPID | Process program ID | Limited to a maximum of 80 bytes.

## Slide 51
4. SECS Message Stream & Functions
■ S7, F18 Delete Process Program Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <ACKC7> |  | 
 | Dictionary |  | 
 | ACKC7 | Acknowledge code, 1 byte | 0 = Accepted 1 = Permission not granted 2 = Length error 3 = Matrix overflow 4 = PPID not found 5 = Mode unsupported 6 = Command will be performed with completion signaled later >6 = Other error 7-63 Reserved
■ S7, F19 Current EPPD Request (H → E) | 
 | Description
 | This message is used to request the transmission of the current equipment process program directory (EPPD). This is a list of all the PPIDs of the process programs stored in the equipment.
 | Structure
 | Header only
■ S7, F20 Current EPPD Data (H ← E) |  |  | 
 | Description |  | 
 | This message is used to transmit the current EPPD. |  | 
 | Structure |  | 
 | L,n (number of process programs in the directory) 1. <PPID1> . . n. <PPIDn> |  | 
 | Note |  | 
 | Dictionary |  | 
 | PPID | Process program ID | Limited to a maximum of 80 bytes.

## Slide 52
4. SECS Message Stream & Functions
■ S7, F23 Formatted Process Program Send (H ↔ E) |  |  | 
 | Description |  | 
 | This message allows movement of formatted process programs between a piece of equipment and its host system. |  | 
 | Structure |  | 
 | L,5 1. <PPID> 2. <MDLN> 3. <SOFTREV> 4. L,c (c = Number of Process Commands) 1. L,2 1. <CCODE> 2. L,p (p = Number of Parameters) 1. <PPARM1> . . p. <PPARMp> 2. L,2 . . c. L,2 |  | 
 | Note |  | 
 | Dictionary |  | 
 | PPID | Process program ID | Limited to a maximum of 80 bytes.
 | MDLN | Equipment Model Type, 6 bytes max | Same data as returned by S1,F2
 | SOFTREV | Software revision code 6 bytes maximum | 
 | CCODE | Command Code | 
 |  | Process Parameter | Numeric or Boolean SECS data item, single or multiple value, or text string which provides information required to complete the process command to which the parameter refers.
■ S7, F24 Formatted Process Program Acknowledge (H ↔ E) |  |  | 
 | Structure |  | 
 | <ACKC7> |  | 
 | Dictionary |  | 
 | ACKC7 | Acknowledge code, 1 byte | 

## Slide 53
4. SECS Message Stream & Functions
■ S7, F26 Formatted Process Program Data (H ↔ E) |  |  | 
 | Description |  | 
 | This message transfers a process program in response to a request for the PPID. |  | 
 | Structure |  | 
 | L,4 1. <PPID> 2. <MDLN> 3. <SOFTREV> 4. L,c (c = Number of Process Commands) 1. L,2 1. <CCODE> 2. L,p (p = Number of Parameters) 1. <PPARM1> . . p. <PPARMp> 2. L,2 . . c. L,2 |  | 
 | Note |  | 
 | A zero length list indicates the request was denied. |  | 
 | Dictionary |  | 
 | PPID | Process program ID | Limited to a maximum of 80 bytes.
 | MDLN | Equipment Model Type, 6 bytes max | Same data as returned by S1,F2
 | SOFTREV | Software revision code 6 bytes maximum | 
 | CCODE | Command Code | 
 |  | Process Parameter | Numeric or Boolean SECS data item, single or multiple value, or text string which provides information required to complete the process command to which the parameter refers.
■ S7, F25 Formatted Process Program Request (H ↔ E) |  |  | 
 | Description |  | 
 | This message is used by either equipment or host to request a particular process program from the other. |  | 
 | Structure |  | 
 | <PPID> |  | 
 | Dictionary |  | 
 | PPID | Process program ID | Limited to a maximum of 80 bytes.

## Slide 54
4.7 STREAM 9
■ S9, F1 Unrecognized Device ID (H ← E) |  |  | 
 | Description |  | 
 | Device ID specified in block header is not defined in the machine. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
■ S9, F3 Unrecognized Stream Type (H ← E) |  |  | 
 | Description |  | 
 | Machine does not recognize the stream type in the message block header. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
■ S9, F5 Unrecognized Function Type (H ← E) |  |  | 
 | Description |  | 
 | Machine does not recognize the stream type in the message block header. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
4. SECS Message Stream & Functions

## Slide 55
■ S9, F9 Transaction Timer Timeout (H ← E) |  |  | 
 | Description |  | 
 | This error specifies that a transaction / receive timer has timed out and the transaction aborted. The host system should respond to this message in a suitable manner to keep the system operational |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
■ S9, F11 Data Too Long (H ← E) |  |  | 
 | Description |  | 
 | The machine has been sent more data than it can handle. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
■ S9, F7 Illegal Data (H ← E) |  |  | 
 | Description |  | 
 | This error signifies that the stream and function were correctly interpreted but the associated data was not. |  | 
 | Structure |  | 
 | <Bi MHEAD> |  | 
 | Dictionary |  | 
 | MHEAD | SECS message block header associated with message block in error | 
4. SECS Message Stream & Functions

## Slide 56
4.8 STREAM 10
■ S10, F3 Terminal Display (Single) (H → E) |  |  | 
 | Description |  | 
 | The host requests a text message be displayed on the machine. |  | 
 | Structure |  | 
 | L , 2 1. <Bi TID> 2. <A TEXT> |  | 
 | Dictionary |  | 
 | TID | Terminal number, 1 byte | 0 = Single or main terminal >0 = Additional terminals at the same equipment
 | TEXT | A single line of characters | 
4. SECS Message Stream & Functions
■ S10, F4 Terminal Display (Single) Acknowledge (H ← E) |  |  | 
 | Structure |  | 
 | <Bi ACKC10> |  | 
 | Dictionary |  | 
 | ACKC10 | Acknowledge Code, 1 byte | 0 = Accepted for display 1 = Message will not be displayed 2 = Terminal not available 3-63 Reserved

## Slide 57
5. SCENARIO
5.1 Message Scenario
■ Host Attempts to Establish Communications
Comment | Host | Equipment | Comment
Establish Communications | S1, F13 |  | 
 |  |  | Communications state is enabled (any substate)
 |  | S1, F14 | Reply COMMACK = Accept and Communications state = COMMUNICATING
Comment | Host | Equipment | Comment
 |  |  | Communications State = NOT COMMUNICATING
 |  | S1, F13 | [LOOP] [LOOP] -- SEND Establish Communications Request
Establish Communications Acknowledge | S1, F14 |  | [IF] S1, F14 received without timeouts [THEN] exit loop -- SEND [ELSE] Delay for interval in EstablishCommunications Timeout [ENDIF] [END_LOOP]--SEND [IF] COMMACK = Accept [THEN] Communications state = Communicating exit loop -- [ELSE] Reset timer for delay, and delay for interval specified in EstablishCommunications Timeout [ENDIF] [END_LOOP]
■ Equipment Attempts To Establish Communications and Host Acknowledges

## Slide 58
Comment | Host | Equipment | Comment
 |  |  | Communications State = NOT COMMUNICATING
 |  | S1, F13 | Establish Communications Request
Establish Communications Request | S1, F13 |  | 
Reply COMMACK = Accept | S1, F14 |  | S1, F14 received from Host and Communications established* and Communications state = COMMUNICATING
 |  | S1, F14 | Reply COMMACK = Accept*
■ Equipment Receives S1, F14 From Host Before Sending S1, F14
Comment | Host | Equipment | Comment
 |  |  | Communications State = NOT COMMUNICATING
 |  | S1, F13 | Establish Communications Request
Establish Communications Request | S1, F13 |  | 
Reply COMMACK = Accept |  | S1, F14 | Reply COMMACK = Accept* Communications established** and Communications state = COMMUNICATING
 | S1, F14 |  | S1, F14 received from Host
■ Equipment Sends S1, F14 To Host Before Receiving S1, F14
5. SCENARIO

## Slide 59
Comment | Host | Equipment | Comment
Send report definitions | S2, F33 |  | DATAIDs, RPTIDs and VIDs received
 |  | S2, F34 | DRACK* = 0 the reports are OK
[ENDIF] |  |  | 
Link reports to events | S2, F35 |  | CEIDs and the corresponding RPTIDs are received
 |  | S2, F36 | LRACK = 0 the event linkages are acceptable.
Enable specific collection events | S2, F37 |  | Enable/disable codes (CEEDs) and the respective event reporting CEIDs received.
 |  | S2, F38 | ERACK = 0 OK, will generate the specified reports when the appropriate collection events happen.
■ Collection Event Reporting Set-up
5. SCENARIO

## Slide 60
Comment | Host | Equipment | Comment
Host requests report of selected status variable values. | S1, F3 |  | 
 |  | S1, F4 | Equipment responds with the requested status variable data.
■ Request Equipment Status Variable Namelist
Comment | Host | Equipment | Comment
Host requests equipment to identify selected status variables. | S1, F11 |  | 
 |  | S1, F12 | Equipment responds with the requested status variable descriptions.
■ Request Equipment Status Report
5. SCENARIO

## Slide 61
Comment | Host | Equipment | Comment
Enable/Disable Alarm | S5, F3 |  | 
 |  | S5, F4 | Acknowledge
■ Enable/Disable Alarms
Comment | Host | Equipment | Comment
Request alarm data/text | S5, F5 |  | 
 |  | S5, F6 | Send alarm data/text
■ Enable/Disable Alarms
Comment | Host | Equipment | Comment
Request enabled alarms | S5, F7 |  | 
 |  | S5, F8 | Send alarm data/text
■ Enable/Disable Alarms
Comment | Host | Equipment | Comment
 |  | S5, F1 | Send alarm report (if enabled)
Acknowledge | S5, F2 |  | 
 |  | S6, F11 | Send event report (if enabled)
Acknowledge | S6, F12 |  | 
■ Send Alarm Report
5. SCENARIO

## Slide 62
Comment | Host | Equipment | Comment
Host Command Send | S2, F41 |  | Remote Command Message
 |  | S2, F42 | Host Command Acknowledge
 |  | S6, F11 | [IF] Command Accepted (HCACK = 0 or 4) [THEN] State change or other collection event Occurrence
Event Report Acknowledge | S6, F12 |  | 
■ Host sends a remote command message
Comment | Host | Equipment | Comment
Host sends equip-ment constants. | S2, F15 |  | 
 |  | S2, F16 | EAC = 0 equipment sets constants
■ Host Equipment Constants Request
Comment | Host | Equipment | Comment
Host constant request | S2, F13 |  | 
 |  | S2, F14 | Equipment constant data, see note below
■ Host sends a remote command message
5. SCENARIO

## Slide 63
Comment | Host | Equipment | Comment
Host constant namelist request | S2, F29 |  | 
 |  | S2, F30 | Equipment
■ Operator Changes Equipment Constant
Comment | Host | Equipment | Comment
 |  |  | Operator changes equipment constant at equipment operator console.
 |  | S6, F11 | Equipment reports equipment constant change.
Host acknowledges event | S6, F12 |  | 
■ Host Equipment Constant Namelist Request
Comment | Host | Equipment | Comment
 |  |  | Material is sent or received at an equipment port.
 |  | S6, F11 | Send Collection event to host
Host acknowledges | S6, F12 |  | 
■ Material Movement
5. SCENARIO

## Slide 64
5. SCENARIO
Comment | Host | Equipment | Comment
 |  |  | New process program created, edited or deleted by operator of equipment. PPChangeName = PPID PPChangeStatus = 1 (Created) = 2 (Edited) = 3 (Deleted)
 |  |  | [IF] CEID for Process Program Change Event enabled [THEN]
 |  | ◄ S6, F11 | Send Event Report
Event Report Acknowledges | S6, F12 ► |  | 
■ Program Created, Edited or Deleted by Operator
Comment | Host | Equipment | Comment
Delete Process Program Send | S7, F17 ► |  | 
 |  | ◄ S7, F18 | The process program is removed from non-volatile storage. Delete Process Program Acknowledge.
■ Process Program Deletion by Host
Comment | Host | Equipment | Comment
Current EPPD Request | S7, F19 ► |  | 
 |  | ◄ S7, F20 | Current EPPD Data
■ Process Program Directory Request

## Slide 65
5. SCENARIO
Comment | Host | Equipment | Comment
Formatted Process Program Request | S7, F25 ► |  | 
 |  | ◄ S7, F26 | Formatted Process Program Data
■ Host-Initiated Process Program Upload
Comment | Host | Equipment | Comment
 |  | ◄ S7, F23 | Formatted Process Program Send
Formatted Process Program Acknowledge | S7, F24 ► |  | 
■ Equipment-Initiated Process Program Upload
Comment | Host | Equipment | Comment
Process Program Load Inquire | S7, F1 ► |  | 
 |  | ◄ S7, F2 | Formatted Process Program Load Grant
Formatted Process Program Send | S7, F23 ► |  | 
 |  | ◄ S7, F24 | Formatted Process Program Acknowledge
■ Host-Initiated Process Program Download
Comment | Host | Equipment | Comment
 |  | ◄ S7, F25 | Formatted Process Program Request
S7,F26 Formatted Process Program Data | S7, F26 ► |  | 
■ Equipment-Initiated Process Program Download

## Slide 66
■ Terminal Services
Comment | Host | Equipment | Comment
Host sends textual information to equipment for display to the operator on terminal x. | S10, F3 |  | 
 |  | S10, F4 | Equipment acknowledges request to display text (equipment sets unrecognized message indicator).
 |  |  | Operator indicates message recognition (equipment clears unrecognized message indicator).
 |  | S6, F11 | Message recognition event. (see Event Data Collection for details).
Host acknowledges Optional: | S6, F12 |  | 
5. SCENARIO

## Slide 67
Comment | Host | Equipment | Comment
Host sends textual information to equipment for display to the operator on terminal x. | S10, F3 |  | 
 |  | S10, F4 | Equipment acknowledges request to display text (equipment sets unrecognized message indicator).
Host sends textual information to equipment for display to the operator on ter-minal x. This message overwrites the first one sent by the host since it is still unrecognized. | S10, F3 |  | 
 |  | S10, F4 | Equipment acknowledges request to display text (equipment sets unrecognized message indicator).
 |  |  | Operator indicates message recognition. (Equipment clears unrecognized message indicator).
 |  | S6, F11 | Message recognition event
Host acknowledges | S6, F12 |  | 
5. SCENARIO

## Slide 68
Comment | Host | Equipment | Comment
 |  | S2, F17 | Equipment requests a time value from the host.
Host responds with a TIME value | S2, F18 |  | Equipment sets its internal time reference to the value of TIME received from the host.
■ Host Instructs Equipment to Set Time
Comment | Host | Equipment | Comment
Host instructs equip-ment to set its time. | S2, F31 |  | 
 |  | S2, F32 | The equipment sets its internal time reference to the value of TIME received from the host and acknowledges completion.
■ Host Requests Equipment’s Current Time Value
Comment | Host | Equipment | Comment
Host requests equipment time.. | S2, F17 |  | 
 |  | S2, F18 | Equipment returns its internal time reference value to the host.
■ Equipment Requests TIME (Optional Scenario)
5. SCENARIO

## Slide 69
Comment | Host | Equipment | Comment
 |  |  | Operator actuates ON-LINE switch when equipment OFF_LINE state is active.
 |  | S1, F1 | Equipment request ON-LINE.
Host grants ON-LINE | S1, F2 |  | 
 |  | S6, F11 | "Control State LOCAL (or REMOTE)" collection event.
Acknowledge | S6, F12 |  | 
Comment | Host | Equipment | Comment
 |  |  | Operator actuates OFFLINE switch when equipment ON_LINE state is active.
 |  | S6, F11 | "Equipment request OFF-LINE" event.
Acknowledge | S6, F12 |  | 
■ Host Denies ON-LINE
Comment | Host | Equipment | Comment
 |  |  | Operator actuates ONLINE switch when equipment OFF_LINE state is active.
 |  | S1, F1 | Equipment requests ON-LINE.
Host denies ON-LINE | S1, F0 |  | 
■ Operator Sets OFF-LINE
■ Host Accepts ON-LINE
5. SCENARIO

## Slide 70
Comment | Host | Equipment | Comment
Host request OFF-LINE. | S1, F15 |  | 
 |  |  | [IF] Equipment is OFF-LINE
 |  | S1, F0 | [THEN] Equipment does not process requests.
 |  |  | [ELSE] Equipment ON-LINE
 |  | S1, F16 | Equipment acknowledges request and transitions to OFF-LINE.
 |  | S6, F11 | "Equipment OFF-LINE" event.
Acknowledge | S6, F12 |  | 
 |  |  | [END_IF]
Comment | Host | Equipment | Comment
 |  |  | Operator sets switch from LOCAL to REMOTE.
 |  | S6, F11 | "Control State REMOTE" event..
Acknowledge | S6, F12 |  | 
■ Operator Sets REMOTE
■ Operator Sets LOCCAL
Comment | Host | Equipment | Comment
` |  |  | Operator sets switch from REMOTE to LOCAL.
 |  | S6, F11 | "Control State LOCAL" event..
Acknowledge | S6, F12 |  | 
■ Host Sets OFF-LINE
5. SCENARIO

## Slide 71
Comment | Host | Equipment | Comment
Host requests ON-LINE. | S1, F17 |  | 
 |  |  | [IF] Equipment is HOST OFF-LINE state not active.
 |  | S1, F18 | [THEN] Equipment denies request (ONLACK = 0).
 |  |  | [ELSE] Equipment HOST OFF-LINE state is active.
 |  | S1, F18 | Equipment acknowledges request (ONLACK = 0).
 |  | S6, F11 | "Control state LOCAL (or REMOTE)" event.
Acknowledge | S6, F12 |  | 
 |  |  | [END_IF]
■ Host Sets OFF-LINE
5. SCENARIO

## Slide 72
5.2 Connection Establishment Scenario
HOST
TOOL
Establish Communication Request
Establish Communication
Request Acknowledge
<COMMACK=0,1>
S1F13
S1F14
Request Online
S1F17
S1F18
Online Acknowledge
<ONLACK=0,1,2>
COMMACK = 1
Establish Communication Request
Establish Communication
Request Acknowledge
Until COMMACK=0
S1F13
S1F14
COMMACK = 0
Disable all Events
S2F37
S2F38
Define Reports
S2F33
S2F34
Enable Events
S2F37
S2F38
Data and Time Set Request
S2F31
S2F32
CEED = FALSE
CEED = TRUE
Link Event Reports
S2F35
S2F36
Delete Report Link
S2F35
S2F36
Delete RPTID
S2F33
S2F34
5. SCENARIO
New Equipment Constant
<ECID=101, ECV=‘AP-TG-05’>
S2F15
S2F16
S5F3
S5F4
S5F3
S5F4
ALED = 0 (Disable)
ALED = 1 (Enable)

## Slide 73
■ PAUSE Command (by Host)
5.3 Remote Command Scenario
HOST
TOOL
S2F42
ACK
S6F11
ProcessingStateChanged
< ProcessState=6(Pause)>
5. SCENARIO
S2F41
Host Command (PAUSE)
S6F12
ACK
■ PAUSE Command (by Equipment)
HOST
TOOL
S6F12
ACK
S6F11
ProcessingStateChanged
< ProcessState=6(Pause)>

## Slide 74
5. SCENARIO
■ RESUME Command (by Equipment)
HOST
TOOL
S6F12
ACK
■ RESUME Command (by Host)
HOST
TOOL
S2F42
ACK
S2F41
Host Command (RESUME)
S6F12
ACK
S6F11
ProcessingStateChanged
< ProcessState=1~5>
S6F11
ProcessingStateChanged
< ProcessState=1~5>

## Slide 75
5.5 Normal Scenario
HOST
TOOL
IP01에 Glass 도착
5. SCENARIO
S6F11
ModuleStart
SubstrateLocationOccupied
GlassStart (첫번째 Glass 인 경우 발생)
GlassStartEach (Glass 마다 발생)
SubstrateLocationUnoccupied
ModuleEnd
Glass RS02 로 이동
S6F11
ModuleStart
SubstrateLocationOccupied
ProcessData
(RS02 Recipe Item)
SubstrateLocationUnoccupied
ModuleEnd
Glass RS01 로 이동
S6F11
ModuleStart
SubstrateLocationOccupied
ProcessData
(RS01 Recipe Item)
SubstrateLocationUnoccupied
ModuleEnd
Glass DEV01 로 이동
S6F11
ModuleStart
SubstrateLocationOccupied
ProcessData
(DEV01 Recipe Item)
SubstrateLocationUnoccupied
ModuleEnd

## Slide 76
HOST
TOOL
Glass RS03 로 이동
5. SCENARIO
Glass BF01 로 이동
Glass AK01 로 이동
Glass RS04 로 이동
S6F11
ModuleStart
SubstrateLocationOccupied
ProcessData
(AK01 Recipe Item)
SubstrateLocationUnoccupied
ModuleEnd
S6F11
ModuleStart
SubstrateLocationOccupied
SubstrateLocationUnoccupied
ModuleEnd
S6F11
ModuleStart
SubstrateLocationOccupied
ProcessData
(RS04 Recipe Item)
SubstrateLocationUnoccupied
ModuleEnd
S6F11
ModuleStart
SubstrateLocationOccupied
ProcessData
(RS03 Recipe Item)
SubstrateLocationUnoccupied
ModuleEnd
Glass RS05 로 이동
S6F11
ModuleStart
SubstrateLocationOccupied
ProcessData
(RS05 Recipe Item)
SubstrateLocationUnoccupied
ModuleEnd

## Slide 77
HOST
TOOL
Glass LF01 로 이동
5. SCENARIO
Glass OP01 로 이동
Glass UCV01~ UCV05 로 이동
S6F11
ModuleStart
SubstrateLocationOccupied
GlassEnd (마지막 Glass 인 경우 발생)
GlassEndEach (Glass 마다 발생)
SubstrateLocationUnoccupied
ModuleEnd
S6F11
ModuleStart
SubstrateLocationOccupied
SubstrateLocationUnoccupied
ModuleEnd
S6F11
ModuleStart
SubstrateLocationOccupied
SubstrateLocationUnoccupied
ModuleEnd
Glass EFEM으로 이동
마지막 Glass까지 작업(Glass 투입~배출) 반복